## Slide 1
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE
Chemical Reaction Engineering
By
Dr Salah N. Farhan
Senior lecturer. Chem. Eng. Dept.
College of Engineering
University of Diyala

## Slide 2
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE
Chapter 6
Membrane Reactors

## Slide 3: Membrane – Terminologies
Membrane: A material that allows selective permeation (or passing through) of certain molecules (species).
Permeate: The part of the fluid stream that passes through the membrane.
Retentate: The part of the fluid stream that does not pass through the membrane.
Feed
Retentate
Permeate
Permeate
Membrane
Schematic representation of a membrane separation process

## Slide 4: Membrane Reactors – What and Why?
Usually in a chemical process, the separation of wanted and unwanted species are carried out in a separation vessel downstream of a reactor.
Membrane reactor allows the separation and reaction processes to occur simultaneously and in a single-vessel.
Catalytic membrane reactor can be used to increase the yields of products from reactions that are thermodynamically limited, i.e. from reversible reactions.
Catalytic membrane reactors can be classified into two categories:
  Inert Membrane Reactor with Catalyst on Feed Side
  Catalytic Membrane Reactor

## Slide 5
Inert Membrane Reactor with Catalyst on Feed side (IMRCF)
Membrane
Feed
Permeate
Permeate
Catalyst
reaction is effected by the catalyst present as a pellet or packing.
membrane is inert and merely allows selective permeation of a particular species.
the feed side can be treated simply as a packed bed reactor

## Slide 6
Catalytic Membrane Reactor (CMR)
Feed
Permeate
Permeate
reaction occurs on the membrane surface which acts as a catalyst
membrane is not inert and allows both the selective permeation of a particular species and the reaction catalysis
the feed side can be treated simply as a plug flow reactor, if there are no packings.
Membrane

## Slide 7: Membrane Reactor: General Mole Balance
Reaction: C3H8  C3H6 + H2
A B C
GMBE on A
FA
GMBE on C
Membrane is permeable to C only
FB
FC
RC
GMBE on B
RC = rate of permeation

## Slide 8: Membrane Reactor: Permeation Rate
FA
FB
FC
RC
RC = rate of permeation moles/cm3-s
= f (CA) or f (PA)
For example, hydrogen permeation through Palladium membrane is given by following equation:
Permeation rates are usually determined experimentally.

## Slide 9: Micro-Reactors

## Slide 10
Micro-reactors: It is all about scale
20 m?
Conventional Chemical Plant
Microreactor

## Slide 11: Micro-reactors: Introduction
Generally, we mean:
  Fluid chemical reactants
  Microscale ducts, chambers
  High surface area/vol ratio
  Small volume flowrates
  Precise parameter control
Well-suited for:
  Small-scale output
  In-situ/portable reactors
  High efficiency (yield, thermal efficiency)
  High precision
  e.g., Lab-on-a-chip tech
Oregon State University—
Fractal MECS Devices
Micro-Space Chemistry Lab– Various Microreactors

## Slide 12: Micro-channel Reactors
Reacting mixture flows through the channels
Catalyst coated on channel surface
Salient features of micro-channel reactors
  High heat transfer rate
  High mass transfer rate
  Large reaction area per unit volume
  Low pressure drop

## Slide 13: Micro-channel Reactors

## Slide 14: Micro-Channel Development at ‘Karan Research Group’

## Slide 15: The Role of the Reactor “From Well to Wheel”
Methanol
Supply
Local Storage &
Transport
Reforming
Reactor
CH3OH + H2O  CO2 + 3H2
Separate
H2
Small Fuel Cell
e.g. carbon recycling plant
e.g. a small tank
e.g. palladium membrane
Power to Application

## Slide 16: Micro-channel reactor: alumina substrate
500 mm
30 mm

## Slide 17: Micro-channel reactor: aluminium substrate

## Slide 18: ….Testing Catalyst Activity
Microchannel reactor assembly
Microchannels on a wafer

## Slide 19: Computational Modelling
(Above) Fluid at room temperature enters a heated microchannel and reaches target T=470K in ~10μm.
(Above) Fluid enters microchannel and reaches fully developed (FD) flow in ~10 μm.
Computational simulations have been run to predict channel flow.
Results generally show reactants are quick to reach target temperature.
(Above) Results show flow development in a cross-section of a channel inlet.

## Slide 20: GMBE for a Catalyst Coated Microchannel Reactor
Feed
Catalyst Coating
Circular X-Section
Square X-Section
Derivation to be provided in class

## Slide 21: Semi-Batch Reactors

## Slide 22
Semi-Batch Reactors
B
A
heat
B is slowly fed to A contained in the reactor.
Unwanted products can be minimized
exothermic reaction can be carried out at controlled rate
Product C is continuously removed
Higher conversion for reversible reactions can be obtained
C
A, B

## Slide 23
Selectivity and Yield (Chapter 6)
Instantaneous Global
Selectivity
Yield
Example
Desired Reaction: A + B  D
Undesired Reaction: A + B  U
We can use
a semi-batch reactor
to maximize selectivity
B
A

## Slide 24: Semi-Batch Reactors - GMBE
Reactant that starts in the reactor is always the limiting reactant
There are 3 forms of General Mole Balance Equations for Semi-Batch Reactors
GMBE expressed on a molar basis
GMBE expressed on a concentration basis
GMBE expressed on a conversion basis

## Slide 25: Semi-Batch Reactors - GMBE
1. GMBE on a molar basis
Input - Output + Gen = Accu.
B
FBO
vO
For Species A
For Species B
Constant Density Systems

## Slide 26: Semi-Batch Reactors - GMBE
2. GMBE on a concentration Basis
Input - Output + Gen = Accu.
B
FBO
vO
For Species A
Similarly for Species B

Constant Density Systems

## Slide 27: Semi-Batch Reactors – GMBE
3. GMBE on a conversion Basis
Input - Output + Gen = Accu.
B
FBO
vO
Defining conversion for reactant that is being added (in our case - B) is tricky and perhaps not meaningful.

## Slide 28
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE

## Slide 29
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE

## Slide 30
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE

## Slide 31
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE

## Slide 32
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE

## Slide 33
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE

## Slide 34
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE

## Slide 35
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE

## Slide 36
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE

## Slide 37
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE

## Slide 38
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE

## Slide 39
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE

## Slide 40
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE

## Slide 41
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE

## Slide 42
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE

## Slide 43
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE