## Slide 1
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE
Chemical Reaction Engineering
By
Dr Salah N. Farhan
Senior lecturer. Chem. Eng. Dept.
College of Engineering
University of Diyala

## Slide 2
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE
Chapter 1: Mole Balances
Learning Resources
Learning Resources

## Slide 3: General Algorithm for Solving Isothermal Reactor Problems
General Mole Balance Equation (GMBE)
Rate Laws
  Write down rate law in terms of limiting reactant
Stoichiometry
  relate concentration to volume and number of moles (for batch reactors) or to volumetric flow rate and molar flow rate (for flow reactor)
  Relate volume or volumetric flow rate to conversion (X), pressure and temperature
Combine
  Substitute rate law and stoichiometry in to the GMBE

## Slide 4: General Algorithm for Solving Isothermal Reactor Problems

## Slide 5: Class Problem-4
It is being considered that the following gas-phase reaction be carried out in a CSTR: A + 2B  4C
The reactor will be operated isobarically and isothermally. The rate law for the reaction is given as: (-rA)=k  CACB
where, k = 8 L/mol-min at the operating temperature.
The total feed volumetric flow rate to the reactor at operating temperature and pressure is 10 L/min. The feed consists of A, B and an inert (I). The feed molar flow rates are FA0= FB0= 1 mol/s and FI0=2 mol/s.
Calculate the volume of reactor required to achieve 80% conversion of the limiting reactant.
If all other conditions are kept constant (including total volumetric flow rate) but no inert is present in the feed, calculate the reactor volume required to achieve 80% conversion of limiting reactant

## Slide 6: CSTR-in-series: Introduction to Damkohler Number

## Slide 7: Damkohler Number (Da)
Da is a dimensionless number that can provide a quick estimate of the degree of conversion in continuous flow reactors.
Da  0.1 usually results in conversion less than 10%
Da  10 usually results in conversion greater than 90%
First-order reaction
Second-order reaction

## Slide 8: CSTR in series
Mole Balance on CSTR-1
CAO
X=0
v0
CA1
X=X1
CA2
X=X2
Mole Balance on CSTR-2
V1 ; k1
V2 ; k2
Liquid-phase (v = v0), first-order reaction

## Slide 9: n-Equal Sized CSTR in series
CAO
X=0
v0
CAn
X=Xn
CA n-1
X=Xn-1
V
V
V
V
V
All CSTR’s are operated at same temperature
[ k is same in all reactors]

## Slide 10: n-Equal Sized CSTR in series

## Slide 11: n-Equal Sized CSTR in Parallel
What is the “conversion” of the mixed stream ?
CAO
X=0
v0
CAn
X=Xn
CA2
X=X2
V
V
V
V
CA3
X=X3
C1
X=X1
X = Xmix
vo/n
vo/n
vo/n
vo/n

## Slide 12: ‘n’ Equal-sized CSTRs - Which is a better configuration? Parallel or Series
If you had n-equal sized reactors available and had the option of setting them in series or parallel, which configuration would you choose to achieve maximum conversion for a first-order reaction occurring in liquid phase?
Justify your choice?

## Slide 13: Revisiting Packed Bed Reactors

## Slide 14: Solid Catalyzed Reactions
Reaction rates are usually expressed in terms of mass of catalyst loading.
in mol/time·mass of catalyst
The design equations can be derived in a manner similar to those for homogeneous reactors - by using mass (w) instead of volume (V).
Examples of solid catalyzed reactions:
  Steam Methane Reforming (SMR) for HYDROGEN production
  Conversion of NOx and CO in automobile catalytic converter
  Styrene production

## Slide 15: General Mole Balance for Packed Bed Reactors
Input - Output + Gen = Accumulation
w
w+w
Mass of catalyst = w
FAO
FA

## Slide 16: Pressure Drop in Packed Bed Reactors
Flow of fluids through packed beds is accompanied by substantial pressure drop across the bed.
From reaction perspective, do we need to account for pressure drop in packed bed reactors ?
The answer depends on the type of reaction
  For liquid-phase reactions, small changes in pressure does not affect concentration and consequently does not affect the reaction rates.
  However, for gas-phase reactions, the concentrations are a function of pressure. Reduction in pressure implies reduction in concentration and, consequently, a reduction in reaction rates.

## Slide 17: Relationship between concentration and pressure
Case II: Gas phase reactions
Case I: Liquid phase reactions
v = vO =constant
(ri) = k(T)  f(Concentration)
Concentration does not depend on pressure. No need to calculate pressure to solve for conversion
Inlet Conditions

## Slide 18: Relationship between concentration and pressure
Case II: Gas phase reactions (cont.)
For isothermal reactor
(P/PO) may vary along the reactor length
(ri) = k(T)  f(Concentration)

## Slide 19: Pressure Drop in an Isothermal PBR – Our Approach
Ultimately, we want to write two coupled differential equations that describes how the two variables - conversion (X) and pressure (P) - change with reactor length or mass of catalyst packed
Variation of conversion with catalyst weight
Variation of pressure with catalyst weight
From GMBE
Next, we will review equation describing pressure drop in packed beds

## Slide 20: Pressure Drop in Packed Bed Reactors
ERGUN equation for pressure drop in a packed bed:
Laminar
(NRE < 1)
Turbulent
(NRE > 1000)
Differential equation
for pressure drop in bed of spherical packing

## Slide 21: Pressure Drop in Packed Bed Reactors
In the above equation, some of the parameters are:
  characteristic of the packing [porosity (f), particle (Dp)]
  characteristic of fluid property [viscosity (m), density (r)]
  characteristic of operating parameters [mass velocity (G)]
The packing characteristics are usually considered to be invariant with respect to reactor length.
This leaves us with the following parameters to be evaluated as a function of reactor length
  the fluid properties: viscosity (m) and density (r)
  the operating parameter G
Fixed for a given packed bed
Varies with operating condition and reaction mixture

## Slide 22
Superficial Mass velocity (G)
G is the mass flow rate per unit area (kg/m2-s).
For a reactor with a constant cross-section, G is constant.
Thus, if G is known at inlet it need not be evaluated at any other reactor position z
Here, u and u0 are velocities (in m/s)
NOT to be confused with volumetric flow rate (v)
Evaluating terms in Ergun equation

## Slide 23: Evaluating terms in Ergun equation
Density of gases depend on pressure.
There are two ways of handling the pressure term:
in terms of inlet density, P/Po, T/To
in terms of local P, T and composition
Viscosity of gases are weak function of pressure. We can assume the gas mixture viscosity to be independent of pressure.
The viscosity of gases depend on the mixture composition. In a reactor, mixture composition will change, the gas mixture viscosity will also change.
Density (r)
Viscosity (m)

## Slide 24: Pressure Drop in PBR – Simplified functional form
If numerical method is applied to solve for differential equation, a simpler and more elegant approach is to calculate density at any given position (z) in the reactor using ideal gas law and local conditions:
where,
Average Molecular Weight
of gas mixture

## Slide 25: Pressure Drop in an Isothermal PBR
Our GOAL is to write two coupled differential equations that describes how the two variables - conversion (X) and pressure (P) - change with reactor length or mass of catalyst packed
Variation of conversion with catalyst weight
Variation of pressure with catalyst weight
From GMBE

## Slide 26
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE

## Slide 27
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE

## Slide 28
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE

## Slide 29
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE

## Slide 30
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE

## Slide 31
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE

## Slide 32
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE

## Slide 33
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE

## Slide 34
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE

## Slide 35
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE

## Slide 36
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE