## Slide 1: LECTURE 5
EXTRACTIVE METALLURGY- FIRST CLASS
FERROUS EXTRACTIVE METALLURGY
operations
Steelmaking Process
Integrated steelmaking consist of three phases:
Reduction:
Iron ore, as mined, is a combination of iron with oxygen and various other unwanted substances, generally known as "gangue". The first metallurgical step is to reduce iron ore

## Slide 2: to metallic iron, a process which is
EXTRACTIVE METALLURGY- FIRST CLASS
FERROUS EXTRACTIVE METALLURGY
mostly carried out in a blast furnace,
using coke as both a fuel and reducing agent. The metallic iron produced by such a furnace contains a relatively high proportion of carbon (4%) and is passed to the steelmaking process as a liquid at approximately 1450 C, called "hot metal".
Refining (purifying):

## Slide 3: The refining of iron to make steel is
EXTRACTIVE METALLURGY- FIRST CLASS
FERROUS EXTRACTIVE METALLURGY
where the carbon content of hot metal
is lowered, usually to less than 1 % by an oxidation process in a steelmaking furnace. At the same time, alloying materials are added to the furnace to achieve the required chemical composition of the final product. The chemical content is controlled very carefully during this stage. Originally

## Slide 4: most steel is produced by the most
EXTRACTIVE METALLURGY- FIRST CLASS
FERROUS EXTRACTIVE METALLURGY
modern "basic oxygen steelmaking"
(BOS).
The BOS process uses pure oxygen, injected by a spar (rod), for purifying
the relatively contaminated (impure) hot metal.

## Slide 5
EXTRACTIVE METALLURGY- FIRST CLASS
FERROUS EXTRACTIVE METALLURGY
Shaping & Coating
The liquid steel can then be cast or formed into a variety of solid shapes via the 'continuous
casting' process. The cast steel can then be forged or rolled in successive (following) steps to produce anyone of the many required shapes. Rolling is the most common method of shaping. The modern rolling mill is a huge

## Slide 6: installation, costing millions of dollars and incorporating highly complex electronic control systems. The amount of work to which the steel is
EXTRACTIVE METALLURGY- FIRST CLASS
FERROUS EXTRACTIVE METALLURGY
subjected, and the schedule on which
this work is carried out, have significant effects on its physical characteristics – it dictates (states) whether the steel can be subsequently bent, machined, cut, or

## Slide 7: subjected to any other engineering
EXTRACTIVE METALLURGY- FIRST CLASS
FERROUS EXTRACTIVE METALLURGY
operation, or formed into tubes, pipes
or wire. Once shaped, steel may be coated with other metals such as zinc or tin, or with organic coatings like paint or PVC.
So, steel is made on a large scale by
blowing oxygen and powdered lime through molten iron to oxidize the impurities. According to their use,

## Slide 8: steels are divided into three main groups: Constructional Steel, Tool Steel, Special-Quality Steel (including corrosion-resisting, stainless, acid
EXTRACTIVE METALLURGY- FIRST CLASS
FERROUS EXTRACTIVE METALLURGY
resisting, and heat-resisting steels).
Written by Assist. Lec Athil S. Ibrahim