## Slide 1: Lecture Ten Cupolas
Vertical cylindrical furnace equipped with tapping spout near base
  Used only for cast irons
    Although other furnaces are also used, the largest tonnage of cast iron is melted in cupolas
  The "charge," consisting of iron, coke, flux, and any alloying elements, is loaded through a charging door located less than halfway up height of cupola

## Slide 2
Cupola for melting cast iron

## Slide 3: Direct Fuel‑Fired Furnaces
Small open‑hearth in which charge is heated by natural gas fuel burners located on side of furnace
  Furnace roof assists heating action by reflecting flame down against charge
  At bottom of hearth is a tap hole to release molten metal
  Generally used for nonferrous metals such as copper‑base alloys and aluminum

## Slide 4: Crucible Furnaces
Metal is melted without direct contact with burning fuel mixture
  Sometimes called indirect fuel‑fired furnaces
  Container (crucible) is made of refractory material or high‑temperature steel alloy
  Used for nonferrous metals such as bronze, brass, and alloys of zinc and aluminum
  Three types used in foundries: (a) lift‑out type, (b) stationary, (c) tilting

## Slide 5: Three Types of Crucible Furnaces
(a) Lift‑out crucible, (b) stationary pot - molten metal must be ladled, and (c) tilting-pot furnace

## Slide 6: Electric‑Arc Furnaces
Charge is melted by heat generated from an electric arc
  High power consumption
    But electric‑arc furnaces can be designed for high melting capacity
  Used primarily for melting steel

## Slide 7: Induction Furnaces
Uses alternating current passing through a coil to develop magnetic field in metal
  Induced current causes rapid heating and melting
  Electromagnetic force field also causes mixing action
Since metal does not contact heating elements, environment can be closely controlled to produce molten metals of high quality and purity
Common alloys: steel, cast iron, and aluminum

## Slide 8: Induction Furnace

## Slide 9: Ladles
Two common types of ladles to transfer molten metals to molds: (a) crane ladle, and (b) two‑man ladle

## Slide 10: Additional Steps After Solidification
Trimming
Removing the core
Surface cleaning
Inspection
Repair, if required
Heat treatment

## Slide 11: Trimming
Removal of sprues, runners, risers, parting‑line flash, fins, chaplets, and any other excess metal from the cast part
  For brittle casting alloys and when cross sections are relatively small, appendages can be broken off
  Otherwise, hammering, shearing, hack‑sawing, band‑sawing, abrasive wheel cutting, or various torch cutting methods are used

## Slide 12: Removing the Core
If cores have been used, they must be removed
  Most cores are bonded, and they often fall out of casting as the binder deteriorates
  In some cases, they are removed by shaking the casting, either manually or mechanically
  In rare cases, cores are removed by chemically dissolving bonding agent
  Solid cores must be hammered or pressed out

## Slide 13: Surface Cleaning and Inspection
Removal of sand from casting surface and otherwise enhancing appearance of surface
  Cleaning methods: tumbling, air‑blasting with coarse sand grit or metal shot, wire brushing, buffing, and chemical pickling
  Surface cleaning is most important for sand casting
  Defects are possible in casting, and inspection is needed to detect their presence

## Slide 14: Heat Treatment
Castings are often heat treated to enhance properties
Reasons for heat treating a casting:
  For subsequent processing operations such as machining
  To bring out the desired properties for the application of the part in service