## Slide 1: Lecture Tow Chapter 2 METAL CASTING PROCESSES
Sand Casting
Other Expendable Mold Casting Processes
Permanent Mold Casting Processes
Foundry Practice
Casting Quality
Metals for Casting
Product Design Considerations

## Slide 2: Two Categories of Casting Processes
Expendable mold processes - mold is sacrificed to remove part
  Advantage: more complex shapes possible
  Disadvantage: production rates often limited by the time to make mold rather than casting itself
Permanent mold processes - mold is made of metal and can be used to make many castings
  Advantage: higher production rates
  Disadvantage: geometries are limited by the need to open the mold

## Slide 3: Overview of Sand Casting
Most widely used casting process, accounting for a significant majority of total tonnage cast
Nearly all alloys can be sand casted, including metals with high melting temperatures, such as steel, nickel, and titanium
Castings range in size from small to very large
Production quantities from one to millions

## Slide 4
Sand casting for an industrial pump. Holes and surfaces have been machined (courtesy of George E. Kane Manufacturing Technology Laboratory, Lehigh University)

## Slide 5: Steps in Sand Casting
Pour the molten metal into sand mold
Allow time for metal to solidify
Break up the mold to remove casting
Clean and inspect casting
  Separate gating and riser system
Heat treatment of casting is sometimes required to improve metallurgical properties

## Slide 6: Making the Sand Mold
The cavity in the sand mold is formed by packing sand around a pattern, then separating the mold into two halves and removing the pattern
The mold must also contain gating and riser system
If casting is to have internal surfaces, a core must be included in mold
A new sand mold must be made for each part produced

## Slide 7: Sand Casting Production Sequence
Production sequence in sand casting, including pattern‑making and mold‑making

## Slide 8: The Pattern
Full‑sized model of the part, slightly enlarged to account for shrinkage and machining allowances in the casting
Pattern materials:
  Wood - common material because it is easy to work, but it warps
  Metal - more expensive to fabricate, but lasts longer
  Plastic - compromise between wood and metal

## Slide 9: Types of Patterns
Types of patterns used in sand casting: (a) solid pattern, (b) split pattern, (c) match‑plate pattern, (d) cope and drag pattern

## Slide 10: Core
Full‑scale model of interior surfaces of part
  Inserted into mold cavity prior to pouring
  The molten metal flows and solidifies between the mold cavity and the core to form the casting's external and internal surfaces
  May require supports to hold it in position in the mold cavity during pouring, called chaplets

## Slide 11: Core in Mold
(a) Core held in place in the mold cavity by chaplets, (b) possible chaplet design, (c) casting