## Slide 1: Lecture Four Other Expendable Mold Processes
Shell Molding
Vacuum Molding
Expanded Polystyrene Process
Investment Casting
Plaster Mold and Ceramic Mold Casting

## Slide 2: Shell Molding
Casting process in which the mold is a thin shell of sand held together by thermosetting resin
Steps: (1) A metal pattern is heated and placed over a box containing sand mixed with TS resin

## Slide 3: Steps in Shell Molding
(2) Box is inverted so that sand and resin fall onto the hot pattern, causing a layer of the mixture to partially cure on the surface to form a hard shell

## Slide 4: Steps in Shell Molding
(3) Box is repositioned so loose uncured particles drop away

## Slide 5: Steps in Shell Molding
(4) Sand shell is heated in oven for several minutes to complete curing

## Slide 6: Steps in Shell Molding
(5) shell mold is stripped from pattern

## Slide 7: Steps in Shell Molding
(6) Two halves of the shell mold are assembled, supported by sand or metal shot in a box, and pouring is accomplished

## Slide 8: Steps in Shell Molding
(7) Finished casting with sprue removed

## Slide 9: Shell Molding: Advantages and Disadvantages
Advantages:
  Smoother cavity surface permits easier flow of molten metal and better surface finish
  Good dimensional accuracy
  Mold collapsibility minimizes cracks in casting
  Can be mechanized for mass production
Disadvantages:
  More expensive metal pattern
  Difficult to justify for small quantities