## Slide 1: Lecture Nine Squeeze Casting
Combination of casting and forging in which a molten metal is poured into a preheated lower die, and the upper die is closed to create the mold cavity after solidification begins
  Differs from usual closed-mold casting processes in which die halves are closed before introduction of the molten metal
  Compared to conventional forging, pressures are less and finer surface details can be achieved

## Slide 2: Semi-Solid Metal Casting
Family of net-shape and near net-shape processes performed on metal alloys at temperatures between liquidus and solidus
  Thus, the alloy is a mixture of solid and molten metals during casting (mushy state)
  To flow properly, the mixture must consist of solid metal globules in a liquid
    Achieved by stirring the mixture to prevent dendrite formation

## Slide 3: Semi-Solid Metal Casting: Advantages
Complex part geometries
Thin part walls possible
Close tolerances
Zero or low porosity, resulting in high strength of the casting

## Slide 4: Centrifugal Casting
A family of casting processes in which the mold is rotated at high speed so centrifugal force distributes molten metal to outer regions of die cavity
  The group includes:
    True centrifugal casting
    Semicentrifugal casting
    Centrifuge casting

## Slide 5: True Centrifugal Casting
Molten metal is poured into rotating mold to produce a tubular part
  In some operations, mold rotation commences after pouring rather than before
  Parts: pipes, tubes, bushings, and rings
  Outside shape of casting can be round, octagonal, hexagonal, etc , but inside shape is (theoretically) perfectly round, due to radially symmetric forces

## Slide 6: True Centrifugal Casting
Setup for true centrifugal casting

## Slide 7: Semicentrifugal Casting
Centrifugal force is used to produce solid castings rather than tubular parts
  Molds use risers at center to supply feed metal
  Density of metal in final casting is greater in outer sections than at center of rotation
  Often used on parts in which center of casting is machined away, thus eliminating the portion where quality is lowest
    Examples: wheels and pulleys

## Slide 8: Semicentrifugal Casting

## Slide 9: Centrifuge Casting
Mold is designed with part cavities located away from axis of rotation, so molten metal poured into mold is distributed to these cavities by centrifugal force
  Used for smaller parts
  Radial symmetry of part is not required as in other centrifugal casting methods

## Slide 10: Centrifuge Casting
(a) The process and (b) one of the parts cast

## Slide 11: Furnaces for Casting Processes
Furnaces most commonly used in foundries:
  Cupolas
  Direct fuel‑fired furnaces
  Crucible furnaces
  Electric‑arc furnaces
  Induction furnaces