## Slide 1
Chapter Three
Steady Heat Conduction
3.1- Steady Heat Conduction in Plane Walls
Consider a plane wall of thickness L and average thermal conductivity k. The two surfaces of the wall are maintained at constant temperatures of T1 and T2. For one-dimensional steady heat conduction through the wall, we have that T=T(x) only. Then Fourier’s law of heat conduction for the wall can be expressed as;
Q
cond, wall
 k A dT (W ) (3.1)
dx
where the rate of conduction heat transfer Qcond, wall and the wall area A
are constant. Thus we have dT/dx=constant, which means that the temperature through the wall varies linearly with x, as shown in Fig.(3.1). By Separating the variables in the above equation and integrating from x=0, where T(0)= T1, to x=L, where T(L)=T2, we get;


2
T T1
L T
x0
cond , wall
dx   k A dT
Q
By performing above integrations and rearranging gives;
(W ) (3.2)
L
Q
cond , wall
 k A T1  T2
Note1- As we say in chapter1, and as it is clear from above equation, the rate of heat conduction through a plane wall is proportional to the average thermal conductivity, the wall area, and the temperature difference, but is inversely proportional to the wall thickness.
Note2- If the rate of heat conduction is available, the temperature T(x) at any location x can be determined by replacing T2 in Eq.(3.2) by T, and L by x.
3.1.1- The Thermal Resistance Concept
Fourier’s law [Eq.(3.2)] for heat conduction through a plane wall can be rearranged as;
R
cond, wall
cond, wall
(W ) (3.3.a)
Q
 T1  T2
where;
k A
R
cond , walll
(C  / W ) (3.3.b)
 L
which is the thermal resistance of the wall against heat conduction or simply the conduction resistance of the wall.
Note1- The thermal resistance of a medium depends on the geometry
and the thermal properties of that medium.
Note2- The equation above for conduction heat flow is analogous to the relation of Ohm's law for electric current flow I, which expressed as;
( Amp) (3.4)
Re
I  V1  V2
where Re is the electric resistance and V1 - V2 is the voltage difference across the resistance. Thus, the rate of heat transfer through a layer corresponds to the electric current, the thermal resistance corresponds to electrical resistance, and the temperature difference corresponds to voltage difference across the layer as shown in Fig.(3.2).
Fig.(3.2) Analogy between thermal and electrical resistance concepts
Fig.(3.1) Under steady conditions, the temperature distribution in a plane wall is a straight line

## Slide 2
Chapter Three
Steady Heat Conduction
Note3- Consider convection heat transfer from a solid surface of area As and temperature Ts to a fluid whose temperature is T∞, with a convection heat transfer coefficient h. Newton’s law of cooling for
convection heat transfer rate Qconv  h As (Ts T ) can be rearranged as;
R
conv
conv
(W ) (3.5.a)
Q
 Ts  T
where;
h A
R
s
conv
(C  / W ) (3.5.b)
 1
is the thermal resistance of the surface against heat convection, or simply the convection resistance of the surface as shown in Fig.(3.3).
Fig.(3.3) Schematic for convection resistance at a surface
Note4- When the wall is surrounded by a gas, the radiation effects, which we have ignored so far, can be significant and may need to be considered. The rate of radiation heat transfer between a surface of emissivity ε and area As at temperature Ts and the surrounding surfaces at some average temperature Tsurr can be expressed as;
R
rad
rad
(W ) (3.6.a)
Q
)  Ts  Tsurr
   A (T 4  T 4 )  h A (T  T
s s surr rad s s surr
where;
h A
R
rad s
rad
(K  /W ) (3.6.b)
1
is the thermal resistance of a surface against radiation, or the radiation resistance, and;
s s surr
rad
Qrad
A (T  T )
h 
   (T 2  T 2 )(T  T ) (W / m2 K  ) (3.6.c)
s surr s surr
is the radiation heat transfer coefficient. Note that both Ts and Tsurr must be in K° in the evaluation of hrad.
Note5- A surface exposed to the surrounding air involves convection and radiation simultaneously, and the total heat transfer at the surface is determined by adding (or subtracting, if in the opposite direction) the radiation and convection components. The convection and radiation resistances are parallel to each other, as shown in Fig.(3.4), and may cause some complication in the thermal resistance network. When Tsurr ≈ T∞, the radiation effect can properly be accounted for by replacing h in the convection resistance relation by;
combined conv rad
h  h  h (W / m2 K  ) (3.7)
where hcombined is the combined heat transfer coefficient.
Fig.(3.4) Schematic for convection
and radiation resistances at a surface
3.1.2- Thermal Resistance Network
Now consider steady one-dimensional heat flow through a plane wall of thickness L, area A, and thermal conductivity k that is exposed to convection on both sides to fluids at temperatures T∞1 and T∞2 with heat transfer coefficients h1 and h2, respectively, as shown in Fig.(3.5). Assuming T∞1 > T∞2, the variation of temperature will be as shown in the figure. Under steady conditions we have;



 
 

 
 




from the wall 
   Rate of 
through the wall 
into the wall
 heat convection    heat conduction    heat convection
 Rate of Rate of

## Slide 3
Chapter Three
Steady Heat Conduction
or;
2
1 2
L
)  (3.8.a)
2  2
1 1 1
 h A (T  T
T  T
T )  k A
Q  h A (T
Rconv ,1 Rcond , wall Rconv , 2
 (3.8.b)
which can be rearranged as;
Q  T1  T1  T1  T2  T2  T 2
1 /( h1 A) L /(k A) 1 /(h2 A)
 T1  T1  T1  T2  T2  T 2
(W ) (3.9.a)
or it can be represented in terms of total thermal resistance Rtotal as follow;
Q  T1  T 2
Rtotal
where;
1
h A k A h A
total conv ,1 cond , wall conv , 2
(C  / W ) (3.9.b)
 1  L  1
R  R  R  R
2
Note- It is sometimes convenient to express heat transfer through a medium in an analogous manner to
Newton’s law of cooling as follow;
Q U A Ttotal (W ) (3.10.a)
where U is the overall heat transfer coefficient. A comparison of Eqs. (3.10.a) and (3.9.a) shows that;
or;
1
L 1
h1 A k A h2 A
1
Rtotal A
1
Rtotal
(3.10.b)
(W / m 2 C  )
1
1  L  1

U 
 
 1
U A 
h1 k h2
Therefore, for a unit area, the overall heat transfer coefficient is equal to the inverse of the total thermal resistance.
Fig.(3.5) The thermal resistance network for heat transfer through a plane wall subjected to convection on both sides, and the electrical analogy

## Slide 4
Chapter Three
Steady Heat Conduction
(W ) (3.11.a)
3.1.3- Multilayer Plane Walls
Consider a plane wall that consists of two layers (such as a brick wall with a layer of insulation) as shown in Fig.(3.6). The rate of steady heat transfer through this two-layer composite wall can be expressed as;
Q  T1  T 2
h1 A k1 A k2 A h2 A
 (3.11.b)
 1  L1 L2  1
Rtotal
where Rtotal is the total thermal resistance, expressed as;
Rtotal  Rconv ,1  Rwall ,1  Rwall , 2  Rconv , 2
Note1- Above result for the two-layer case is analogous to the single-layer case, except that an additional resistance is added for the additional layer. So, for plane walls that consist of three or more layers we can use this result by adding an additional resistance for each additional layer.
Q
Note2- If the heat rate is known, an unknown surface
temperature Tj at any surface or interface j can be determined as shown in Fig.(3.7) from;
(3.12)
Rtotal , i  j
Q  Ti  T j
where Ti is a known temperature at location i and (Rtotal, i – j) is the total thermal resistance between locations i and j.
Fig.(3.6) The thermal resistance network for heat transfer through a two-layer plane wall subjected to convection on both sides and the evaluation of the surface and interface temperatures when T∞1 and T∞2 are given
Fig.(3.7) Schematic for Example- 3.1
Fig.(3.7).
3.1-

## Slide 5
Chapter Three
Steady Heat Conduction
Fig.(3.8) Schematic for Example- 3.2
Fig.(3.8).
3.2-

## Slide 6
Chapter Three
Steady Heat Conduction
Fig.(3.9) Schematic for Example- 3.3
Fig.(3.9).
3.3-

## Slide 7
Chapter Three
Steady Heat Conduction
Fig.(3.10) Thermal resistance network for two parallel layers
Fig.(3.11) Thermal resistance network for combined series-parallel arrangement
3.1.4- Generalized Thermal Resistance Networks The thermal resistance concept or the electrical analogy can also be used to solve steady heat transfer problems that involve parallel layers or combined series-parallel arrangements. Consider the composite wall shown in Fig.(3.10), which consists of two parallel layers. The thermal resistance network, which consists of two parallel resistances, can be represented as shown in the figure. Noting that the total heat transfer is the sum of the heat transfers through each layer, so, we have; Q  Q  Q  T1  T2  T1  T2 1 2 R R 1 2  (T  T )  1  1   (3.13.a) 1 2  R R   1 2  By using electrical analogy, we get; Q  T1  T2  (3.13.b) Rtotal where; 1  1  1  R  R1R2 (3.13.c) R R R total R  R total 1 2 1 2 Now consider the combined series-parallel arrangement shown in Fig.(3.11). The total rate of heat transfer through this composite system can again be expressed as; Q  T1  T  (3.14 .a ) Rtotal where; Rtotal  R12  R3  Rconv  R1 R2  R  R  (3.14 .b ) R  R 3 conv 1 2 and; R  L1 , R  L2 , R  L3 , R  1 |  |  |  |  |  |  | 
1 | k1 A1 | 2 k A 2 2 | 3 | k3 A3 | conv | hA3 | 
 | 3.4- | Fig.(3.12). |  |  |  |  | 

## Slide 8
Chapter Three
Steady Heat Conduction
By Assistant Lecturer Ahmed N. Al- Musswy
Fig.(3.12) Schematic for Example- 3.4

## Slide 9
Chapter Three
Steady Heat Conduction
3.2- Steady Heat Conduction in Cylinders and Spheres 3.2.1- Single Layer Cylinders and Spheres
Consider a long cylindrical layer (such as a circular pipe) of inner
radius r1, outer radius r2, length L, and average thermal conductivity k as shown in Fig.(3.13). The two surfaces of the cylindrical layer are maintained at constant temperatures T1 and T2. There is no heat generation in the layer and the thermal conductivity is constant. For one-dimensional heat conduction through the cylindrical layer, we have T(r). Then Fourier’s law of heat conduction for heat transfer through the cylindrical layer can be expressed as;
dr
cond, cyl
Q
 k A dT (W ) (3.15.a)
where A = 2πrL is the heat transfer area at location r. Note that A
depends on r, and thus it varies in the direction of heat transfer.
Separating the variables in the above equation and integrating from r =
r1, where T(r1) = T1, to r = r2, where T(r2) = T2, gives;
2
2
A
T
r Q
cond , cyl
 (3.15.b)



T T1
r r1
dr   k dT
Substituting A = 2πrL and performing the integrations gives;
2 1
ln(r / r )
Q
cond , cyl
T1  T2
 2L k (W ) (3.16)
since Qcond,cyl  constant. This equation can be rearranged as;
R
cyl
cond, cyl
(W ) (3.17.a)
Q
 T1  T2
where;
R
cyl
(C  / W )
2L k
 ln(r2 / r1 )
(3.17.a)
is the thermal resistance of the cylindrical layer against heat
conduction, or simply the conduction resistance of the cylinder layer. Note1- The wall of the pipe, whose thickness is rather small, separates two fluids at different temperatures as shown in Fig.(3.14), and thus
the temperature gradient in the radial direction will be relatively large.
Thus heat transfer through the pipe can be modeled as steady and one-
dimensional. The temperature of the pipe in this case will depend on
one direction only (r-direction). This situation is approximated in
practice in long cylindrical pipes and spherical containers.
Note2- We can repeat the analysis above for a spherical layer by taking A = 4πr 2 and performing the integrations in Eq.(3.15.b). The result can be expressed as;
2 1
1 2 1 2
1 2
sph
cond, sph
Q
 (W ) (3.18.a)
r  r R
T  T T  T
 4 r r k
where;
1 2
sph
(C  / W ) (3.18.b)
4 r r k
r2  r1
R 
is the thermal resistance of the spherical layer against heat conduction, or simply the conduction resistance of the spherical layer.
Fig.(3.14) Heat is lost from a hot water pipe to the air outside in the radial direction, and thus heat transfer from a long pipe is one-dimensional
Fig.(3.13) A long cylindrical pipe (or spherical shell) with specified inner and outer surface temperatures T1 and T2

## Slide 10
Chapter Three
Steady Heat Conduction
Note3- If we have a steady one-dimensional heat flow through a cylindrical or spherical layer that is exposed to convection on both sides to fluids at temperatures T∞1 & T∞2 with heat transfer coefficients h1 & h2, respectively, as shown in Fig.(3.15). The thermal resistance network in this case consists of one conduction and two convection resistances in series, just like the one for the plane wall, and the rate of heat transfer under steady conditions can be expressed as;
(W ) (3.19.a)
Q  T1  T2
(3.19.b)
(2 r2 L) h2
1  ln(r2 / r1 ) 1
Rtotal
where for a cylindrical layer;
Rtotal  Rconv,1  Rcyl  Rconv, 2
(3.19.c)
(4 r 2 ) h 4 r r k (4 r 2 ) h
1 1 1 2 2 2
1  r2  r1 1
(2 r1L) h1 2L k
and for a spherical layer;
Rtotal  Rconv,1  R sph  Rconv, 2
Note that A in the convection resistance relation Rconv = 1/(hA) is the surface area at which convection occurs. It is equal to A = 2πrL for a cylindrical surface and A = 4πr 2 for a spherical surface of radius r. Also note that the thermal resistances are in series, and thus the total thermal resistance is determined by simply adding the individual resistances.
3.2.2- Multilayered Cylinders and Spheres
Steady heat transfer through multilayered cylindrical or spherical shells can be handled just like multilayered plane walls which were discussed earlier simply by adding an additional resistance in series for each additional layer. For example, the steady heat transfer rate through the three-layered composite cylinder of length L shown in Fig.(3.16) with convection on both sides can be expressed as;
Rtotal
(W ) (3.20.a)
Q  T1  T2
Fig.(3.16) The thermal resistance network for heat transfer through a three-layered composite cylinder subjected to convection on both sides
Fig.(3.15) The thermal resistance network for a cylindrical
(or spherical) shell subjected to convection from both the inner
and the outer sides

## Slide 11
Chapter Three
Steady Heat Conduction
where Rtotal is the total thermal resistance, expressed as; Rtotal  Rconv,1  Rcyl,1  Rcyl, 2  Rcyl,3  Rconv, 2  1  ln(r2 / r1 )  ln(r3 / r2 )  ln(r4 / r3 )  1 h1 A1 2L k1 2L k2 2L k3 h2 A4 (3.19.b) where A1 = (2π r1 L) and A4 = (2π r4 L). Note1- Equation (3.19.b) can also be used for a three-layered spherical shell by replacing the thermal resistances of cylindrical layers by the corresponding spherical ones. Note2- If Q is known, we can determine any intermediate temperature Tj by applying the relation Q  (Ti Tj ) / Rtotal, i j across any layer or layers such that Ti is a known temperature at location i and Rtotal, i- j is the total thermal resistance between locations i and j as shown in Fig.(3.17). | 
 | Fig.(3.17) The ratio ΔT/R across any layer is equal to Q which remains constant in one-dimensional steady conduction
Fig.(3.18) Schematic for Example- 3.5
Fig.(3.18).
3.5-

## Slide 12
Chapter Three
Steady Heat Conduction

## Slide 13
Chapter Three
Steady Heat Conduction
Fig.(3.19) Schematic for Example- 3.6
Fig.(3.19).
3.6-

## Slide 14
Chapter Three
Steady Heat Conduction
3.2.3- Critical Radius Of Insulation
Adding more insulation for a plane wall always increases the thermal resistance of that wall without increasing the convection resistance since the heat transfer area A is constant. But adding insulation to a cylindrical pipe or a spherical shell, however, is a different matter. The additional insulation increases the conduction resistance of the insulation layer but decreases the convection resistance of the surface because of the increase in the outer surface area for convection. The heat transfer from the pipe may increase or decrease, depending on which effect will dominate. Consider a cylindrical pipe of outer radius r1 whose outer surface temperature T1 is maintained constant as in Fig.(3.20). The pipe is now insulated with a material whose thermal conductivity is k and outer radius is r2. Heat is lost from the pipe to the surrounding medium at temperature T∞, with a convection heat transfer coefficient h. The rate of heat transfer from the insulated pipe to the surrounding air
can be expressed as;
ins conv
ln(r2 / r1 ) 1 2L k h (2 r2 L)

 (3.20)
R  R
Q 
T1  T T1  T
The variation of Q with the outer radius of the insulation r2 is plotted in Fig.(3.21). The value of r2 at which Q reaches a maximum value is determined from the requirement that dQ / dr2  0 (zero slope), where performing that differentiation and solving for r2
yields the critical radius of insulation for a cylindrical body to be;
h
r
cr , cylinder
(m) (3.21.a)
 k
Note1- The discussions above can be repeated for a sphere, where the critical radius of insulation for a spherical shell is;
h
r
cr , sphere
(m) (3.21.b)
 2k
Note2- As it is clear from both equations above, the critical radius of
insulation depends on the thermal conductivity of the insulation k
and the external convection heat transfer coefficient h.
Note3- The rate of heat transfer from the cylinder increases with the addition of insulation for r2 < rcr, and reaches its maximum value when r2 = rcr, after that starts to decrease for r2 > rcr. Thus, insulating the pipe may actually increase the rate of heat transfer from the pipe instead of decreasing it when r2 < rcr.
Fig.(3.20) An insulated cylindrical pipe exposed to convection from the outer surface and the thermal resistance network associated with it
Fig.(3.21) The variation of heat transfer rate with the outer radius of the insulation r2
3.7-
Fig.(3.22) Schematic for Example- 3.7

## Slide 15
Chapter Three
Steady Heat Conduction
Fig.(3.22).

## Slide 16
Chapter Three Steady Heat Conduction
3.3- Heat Transfer from Finned Surfaces
The rate of heat transfer from a surface at a temperature Ts to the surrounding medium at T∞ is
given by Newton’s law of cooling as; Qconv  hAs (Ts T ) , where As is the heat transfer surface area and h is the convection heat transfer coefficient. When the temperatures Ts and T∞ are fixed by design
considerations. So, there are two ways to increase the rate of heat transfer; to increase the convection
heat transfer coefficient h or to increase the surface area As. Increasing h may require the installation of a pump or fan, or replacing the existing one with a larger one, but this approach may or may not be practical. Besides, it may not be too effective. The alternative is to increase the surface area by attaching to the surface extended surfaces called fins made of highly conductive materials such as aluminum. Fins increase heat transfer from a surface by providing a larger surface area to convection and radiation as in the car radiator shown in Fig.(3.23), also There are a variety of fin designs is available as shown in Fig.(3.24).
Fig.(3.23) The thin plate fins of a car radiator greatly increase the rate of heat transfer to the air
Fig.(3.24) Some special fin designs
3.3.1- Fin Equation
Consider a volume element of a fin at location x having a length of Δx, cross-sectional area of Ac, and a perimeter of p, as shown in Fig.(3.25). Under steady conditions, the energy balance on this volume element can be expressed as;


 
  
 
 

  
the element
  Rate of heat 
 the element at x   element at x  x
 conduction into    conduction from the    convection from 
 Rate of heat   Rate of heat
or;
(3.20)
Q cond , x  Qcond , xx  Qconv
where;
Qconv  h As (T  T )  h( p x)(T  T ) (3.21)
Substituting Eq.(3.21) into Eq.(3.21) and dividing by Δx, we obtain;
Q
 
x
Q
 h p(T  T )  0 (3.22.a)
cond , xx cond , x
Taking the limit as Δx 0 gives;
dx
dQ
cond

 h p(T  T )  0 (3.22.b)

From Fourier’s law of heat conduction we have;
cond
Q
 k A dT (3.22.c)
c dx
Fig.(3.25) Volume element of a fin at location x having a length of Δx, cross-sectional area of Ac,
and perimeter of p

## Slide 17
Chapter Three Steady Heat Conduction
where Ac is the cross-sectional area of the fin at location x. Substitution of this relation into Eq.(3.22.b) gives the differential equation governing heat transfer in fins as follow;

 

dx
dx 
d  k A dT   h p(T  T )  0 (3.23)
c
Note- In general, the cross-sectional area Ac and the perimeter p of a fin vary with x, which makes this differential equation too difficult to solve. In the special case of constant cross section and constant thermal conductivity, the differential equation (3.23) reduces to;
2
dx2
a   0 (3.24.a)
d 2 
where;
k Ac
(3.24.b)
a2  h p
and θ = T -T∞ is the temperature excess.
Eq.(3.24.a) is a linear, homogeneous, 2nd order differential equation with constant coefficients, Therefore, the general solution of that equation will be as follow;
1 2
 (x)  C ea x  C e a x (3.25)
where C1 and C2 are arbitrary constants whose values are to be determined from the boundary conditions at the base and at the tip of the fin.
3.3.2- Fin Boundary Conditions
As it is clear from Eq.(3.25), we need only two conditions to determine C1 and C2, and these two conditions are located at;
1- Boundary condition at fin base:
The temperature of the plate to which the fins are attached is normally called as the fin base temperature and its value is usually known, where T= Tb, Therefore, at the fin base we have a specified temperature boundary condition, expressed as;
b b 
 (0)    T  T (3.26)
2- Boundary condition at fin tip
At the fin tip we have several possibilities, including specified temperature, negligible heat loss, convection, and combined convection and radiation as shown in Fig.(3.26). Next, we consider each case separately.
3.3.2.1- Infinitely Long Fin (T tip = T∞)
For a sufficiently long fin of uniform cross section (Ac = constant), the temperature of the fin at the fin tip will approach the environment
(3.27.a)
temperature T∞ and thus θ will approach zero. That is;
 (L)  T (L) T  T T  0, as; L  
By applying these conditions into Eq.(3.25), we get; B.C.1- At x=L=∞, θ=0  0=C1(∞)+C2(0)  C1=0. B.C.2- At x=0, θ=θb  θb = C2(1)  C2=1.
Thus, the required solution for this case is;
b
(3.27.b)
b 
T T
T(x) T  eax  ex h p /(k Ac )
(x)  eax 
Note1- The temperature along the fin in this case will decrease
exponentially from Tb to T∞, as shown in Fig.(3.27).
Fig.(3.26) Boundary conditions at the fin base and the fin tip
Fig.(3.27) A long circular fin of uniform cross-section

## Slide 18
Chapter Three
Steady Heat Conduction
Note2- The steady rate of heat transfer from the entire fin can be determined by applying Fourier’s law of heat conduction at the fin base as follow;
c dx
long fin
Q
c b 
x0
 k A dT  h pk A (T  T ) (3.27.c)
Note3- The rate of heat transfer from the fin could also be determined by
considering heat transfer from a differential volume element of the fin
and integrating it over the entire surface of the fin. That is,
(3.28)

L
x0
A
A
 fin fin
fin
Q
fin fin
 h (x)( pdx)
  h[T (x)  T ]dA   h (x) dA
Fig.(3.28) Under steady conditions, heat transfer from the exposed surfaces of the fin is equal to heat conduction
to the fin at the base
The two approaches described above are equivalent and give the same result since, under steady conditions, the heat transfer from the exposed surfaces of the fin is equal to the heat transfer to the fin at the base as shown in Fig.(3.28).
3.3.2.2- Negligible Heat Loss from the Fin Tip (Insulated fin tip, Q fintip  0 )
Fins are not likely to be so long that their temperature approaches the surrounding temperature at the tip. A more realistic situation is for heat transfer from the fin tip to be negligible since the heat transfer from the fin is proportional to its surface area, and the surface area of the fin tip is usually a negligible fraction of the total fin area. Then the fin tip can be assumed to be insulated, and the condition at the fin tip can be expressed as;
 0 (3.29)
d
dx x L
where the condition at the fin base remains the same as expressed in Eq.(3.26). The application of these two conditions on the general solution Eq.(3.25) yields;
B.C.1- At x  0,   b  b  C1 (1)  C2 (1)  C1  C2  b
dx
1 2 1 2
B.C.2- At x  L, d  0  0  aC eaL  aC eaL  C  C e2aL
Thus, by solving above two equations, we get;
2
1
& C 
C 
b
e2aL 1
b
1 e2aL
, So the total solution will be;

b
1  e2aL e2aL  1
eax e ax

 (x) 
st nd
eaL eaL
By multiplying the 1 term of above equation by and the 2 by respectively, we have;
eaL eaL
b

eaL  eaL eaL  eaL eaL  eaL
eaxe aL e axeaL  e a ( L x)  ea( L x )

 (x) 
Thus, the final solution for insulated fin tip will be as follow;
(3.30)
Tb  T cosh aL
T (x)  T  cosh a(L  x)
The rate of heat transfer from the fin can be determined again from Fourier’s law as follow;
Q
c dx
insulated tip
c b 
x0
 k A dT  h pk A (T  T ) tanh aL (3.31)

## Slide 19
Chapter Three
Steady Heat Conduction
3.3.2.3- Convection (or Combined Convection and Radiation) from Fin Tip
The fin tips, in practice, are exposed to the surroundings, and thus
the proper boundary condition for the fin tip is convection that also includes the effects of radiation. In general, the fin tip area is a small fraction of the total fin surface area, and thus we'll simplify the problem heat loss from the fin tip [as shown in Fig.3.29)] by replacing the fin length L in the relation for the insulated tip case by
(3.32)
a corrected length Lc which is defined as;
A
c
p
c
L  L 
where Ac is the cross-sectional area and p is the perimeter of the fin at the tip.
Note- By using the proper relations for Ac and p, the corrected lengths for rectangular and cylindrical fins are determined to be;
(3.33)
4 
2 

L  L  D 
L  L  t 
c, cylindrica l fin
c, rec tan gular fin
where t is the thickness of the rectangular fins and D is the diameter of the cylindrical fins.
3.3.3- Fin Efficiency
In general, the fin base temperature Tb gradually decreases toward the fin tip, but in an ideal case of zero thermal resistance or infinite thermal conductivity (k → ∞), the temperature of the fin will be uniform at the base value of Tb as in Fig.(3.30). So, the heat transfer from the fin will be maximum in this case and can be expressed as;
(3.34)
Q fin, max  h Afin (Tb  T )
In reality, the temperature of the fin T(x) will drop along the fin, and thus the heat transfer from the fin will be less because of the decreasing in temperature difference T(x)–Tb toward the fin tip, as shown in Fig.(3.30). To account for the effect of this decrease in temperature on heat transfer, we define a fin efficiency as;
 
 the entire fin were at base temperatur e 
 Ideal heat transfer rate from the fin if 
 Actual heat transfer rate from the fin
fin, max
fin
Q
Q fin
 
or;
(3.35)
Q fin   fin Q fin, max   fin h Afin (Tb  T )
c
Fig.(3.29) Corrected fin length L is
defined such that heat transfer from a fin of length Lc with insulated tip is equal to heat transfer from the actual fin of length L with convection at the fin tip
Fig.(3.30) Ideal and actual temperature distribution in a fin
where Afin = Afin (lateral) + Atip is the total surface area of the fin.
Note1- For the cases of constant cross section (Afin= pL) of very long fins and fins with insulated tips,
the fin efficiency can be expressed as;
(3.36.a)
fin, max
long fin
k Ac  1
h A (T  T ) L h p a L

fin b 
h p k Ac (Tb  T )  1
Q
 Qlong fin

(3.36.b)
fin, max
insulated tip

h Afin (Tb  T ) a L
h p k Ac (Tb  T ) tanh aL  tanh aL
Q
 Qinsulated tip


## Slide 20
Chapter Three Steady Heat Conduction
Note2- Eq.(3.36.b) can also be used for fins which are subjected to convection by replacing the fin length L by the corrected length Lc as follow;
(3.36.c)
fin, max c
convective tip
h Afin (Tb  T ) a L
h p k Ac (Tb  T ) tanh aLc  tanh aLc
Q
 Q convective tip 

Note3- Fin efficiency relations are developed for fins of various profiles and are plotted in Fig.(3.31) for fins on a plain surface and in Fig.(3.32) for circular fins of constant thickness. The fin surface area associated with each profile is also given on each figure. For most fins of constant thickness encountered in practice, the fin thickness t is too small relative to the fin length L, and thus, the fin tip area is negligible.
Fig.(3.31) Efficiency of circular, rectangular, and triangular fins on a plain surface of width w
Fig.(3.32) Efficiency of circular fins of length L and constant thickness t

## Slide 21
Chapter Three
Steady Heat Conduction
3.3.4- Fin Effectiveness
The performance of the fins is estimated on the basis of the enhancement in heat transfer relative to the no-fin case. The performance of fins as shown in Fig.(3.33) is expressed in terms of the fin effectiveness εfin which is defined as;
(3.37)


no fin
fin   b 
fin

the surface of area Ab 
 Heat transfer rate from 
 
the fin of base area A
 Heat transfer rate from 
Q
Q

(3.38)
fin
no fin
fin
Q
 
h Ab (Tb  T ) Ab
Q fin   fin h Afin (Tb  T )  Afin 
Note2- To determining the rate of heat transfer from a finned surface, we must consider the unfinned portion of the surface as well as the
fins. Therefore, the rate of heat transfer for a surface containing n fins
can be expressed as;
Qtotal, fin  Qunfin  Q fin
 h Aunfin (Tb  T )   fin h Afin (Tb  T )
 h ( Aunfin   fin Afin )(Tb  T ) (3.39)
Note3- The overall effectiveness for a finned surface is defined as the ratio of the total heat transfer from the finned surface to the heat transfer from the same surface if there were no fins, so, we have;
(3.39)
fin, overall
Ano fin
Q
 Aunfin   fin Afin
h A (T  T )
 
total,no fin no fin b 
Qtotal, fin  h ( Aunfin   fin Afin )(Tb  T )
where Ano fin is the area of the surface when there are no fins, Afin is the total surface area of all the fins on the surface, and Aunfin is the area of the unfinned portion of the surface as shown in Fig.(3.34).
where Ab is the cross-sectional area of the fin at the base and Q no fin
represents the rate of heat transfer from this area if no fins are attached to the surface. However, the use of fins cannot be justified unless εfin is sufficiently larger than 1.
Note1- Both the fin efficiency and fin effectiveness are related to the Fig.(3.33) The effectiveness of a fin
performance of the fin, but they are different quantities. However, they are related to each other by;
Fig.(3.34) Various surface areas associated with a rectangular surface with three fins
3.3.5- Proper Length of a Fin
We may think that the longer fin will produce larger surface area for the fin, and thus, cause higher rate of heat transfer. Therefore, for maximum heat transfer rate, the fin should be infinitely long. However, the temperature drops along the fin exponentially and reaches the environment temperature at some length. The part of the fin beyond this length will not be useful for heat transfer because it is at the temperature of the environment, as shown in Fig.(3.35). Therefore, the so long fins that their temperature approaches the environment temperature cannot be recommended because of the little increase in heat transfer at the tip region which cannot justify the large increase in the weight and cost.

## Slide 22
Chapter Three
Steady Heat Conduction
To get a sense of the proper length of a fin, we compare heat transfer from a fin of finite length to heat transfer from an infinitely long fin under the same conditions. The ratio of these two heat transfers is;
Q fin
Qlong fin

h p k Ac (Tb  T ) tanh aL h p k Ac (Tb  T )
 tanh aL (3.40)
the values of tanhaL are evaluated for some values of aL and the results are given in Table(3.1). We observe from the table that heat transfer from a fin increases with aL almost linearly at first, but the curve reaches a plateau later and reaches a value for the infinitely long fin at about aL=5. We also observe that reducing the fin length by half in that case (from aL=5 to aL=2.5) causes a drop of just 1% in heat transfer with 50% reduction in the size and possibly the cost of the fin. In practice, a fin length that corresponds to about aL = 1 will transfer 76.2% of the heat that can be transferred by an infinitely long fin, and thus it should offer a good compromise between heat transfer performance and the fin size.
Fig.(3.35) Because of the gradual temperature drop along the fin, the region near the fin tip makes little or no contribution to heat transfer
Table (3.1) The variation of heat
transfer from a fin relative to that from an infinitely long fin
EXAMPLE 3.8-
Copper-plate fins of rectangular cross section having a thickness t=1mm, Length L=10mm, and thermal conductivity k=380W/m∙C° are attached to a plane wall
maintained at a temperature Tb=230C°. The fins dissipate heat by convection into ambient at T∞=30C° with a heat transfer coefficient h=40W/m2∙C°. Assuming negligible heat loss from the fin tip determine the fin efficiency.
SOLUTION A fin of the second type (insulated fin tip) with thickness t=1mm, Length L=10mm, Tb=230C°, T∞=30C°, and h=40W/m2∙C°. The efficiency of this fin to be determined.
Assumptions 1 Heat transfer is steady 2 Heat transfer is one-dimensional 3 Thermal conductivities are constants. 4 Heat transfer coefficient incorporates the radiation effects.
Properties The thermal conductivity is constant k=380W/m∙C°
Analysis To determine the fin efficiency, we first calculate the parameter aL as follows;
p  2(b  t )  2
Ac b t t
1


 14 .51m
2h k t
h p
k A
a 
2(40W / m 2  C  ) (380W / m  C  )(10 3 m)
c
a L  (14 .51m 1 )(10 2 m)  0.1451
By using Eq.(3.36.b) we can calculate the efficiency of the insulated tip fin as follow;
 tanh aL  tanh( 0.1451 )  0.993  99.3%
aL 0.1451
fin

EXAMPLE 3.9-
A steel rod of diameter D=2cm, length L=10cm, and thermal conductivity k=50W/m∙C°, is exposed to ambient air at T∞=20C° with a heat transfer coefficient h=30W/m2∙C°. If one end of the rod is maintained at a temperature of 70C°. calculate the heat loss from the rod, also find the temperature at the other end of the rod.
SOLUTION A rod with D=2cm=0.02m and L=10cm=0.1m, is exposed to air with T∞=20 C°, h=30W/m2∙C°, and the one end temperature is Tb=70 C°.

## Slide 23
Chapter Three
Steady Heat Conduction
Assumptions 1 Heat transfer is steady 2 Heat transfer is one-dimensional 3 Thermal conductivities are constants. 4 Heat transfer coefficient incorporates the radiation effects. Properties The thermal conductivity of rod k=50W/m∙C° is constant. Analysis We can assume the rod to be a fin of the second type because it has a finite length. At the beginning we must calculate aL p   D  4 Ac   D 2  D    4  h p 4 h 4 (30W / m 2  C  ) 1 a     10 .95 m k Ac k D (50 W / m  C  )( 0 .02 m ) a L  (10 .95 m 1 )(0.1m )  1.095 By using Eq.(3.36.b) we can calculate the efficiency of the insulated tip fin as follow; Q   Q   tanh aL  h A (T  T )   kAc tanh aL  h ( pL)(T  T ) fin fin fin, max   fin b    b   aL   hp L     hpkA (T  T ) tanh aL  h(D)k (D 2 / 4)(T  T ) tanh aL c b  b   (30W / m 2  C  )( 0.02m)(50W / m  C  )[ (30W / m 2  C  ) 2 / 4](70C   20C  ) tanh(1.095)  6.87W By using Eq.(3.30) we can calculate the temperature at the other end as follow; T (x)  T  cosh a(L  x)  T (L)  20  cosh[10.95(L  L)]  0.6017  T (L)  50.087C  Tb  T cosh aL 70  20 cosh(1.095) | 
3.10- Fig.(3.36). | Fig.(3.36) Schematic for Example- 3.10

## Slide 24
Chapter Three
Steady Heat Conduction

## Slide 25
Chapter Three
Steady Heat Conduction
PROBLEMS
3.1- Consider a 4m-high, 6m-wide, and 0.3m- thick brick wall whose thermal conductivity is
k=0.8W/m·C° . On a certain day, the
temperatures of the inner and the outer surfaces of the wall are measured to be 14C° and 6C°,
respectively. Determine the rate of heat loss through the wall on that day. Answer: 512 W
3.2- Consider a 1.2m-high and 2m-wide glass window whose thickness is 6mm and thermal conductivity is k = 0.78 W/m ·C°. Determine the steady rate of heat transfer through this glass window and the temperature of its inner surface for a day during which the room is maintained at 24C° while the temperature of the outdoors is -
5C°. Take the convection heat transfer
coefficients on the inner and outer surfaces of the
window to be h1 = 10 W/m2 ·C° and h2 = 25 W/m2 ·C°, and disregard any heat transfer by radiation. Answers: 471 W, 4.4C°
3.3- Consider a 1.2m-high and 2m-wide double- pane window consisting of two 3mm-thick layers of glass (k = 0.78 W/m ·C°) separated by a 12mm-wide stagnant air space (k = 0.026 W/m·C°). Determine the steady rate of heat transfer through this double-pane window and the temperature of its inner surface for a day during which the room is maintained at 24C° while the temperature of the outdoors is -5C°. Take the convection heat transfer coefficients on the inner and outer surfaces of the window to be h1 = 10 W/m2 ·C° and h2 = 25 W/m2 ·C°, and disregard any heat transfer by radiation.
Answers: 114 W, 19.2C°
Prob.(3.3)
3.4- Repeat Problem(3.3), assuming the space between the two glass layers is evacuated.
3.5- Consider an electrically heated brick house (k = 0.40 Btu/h ·ft ·F°) whose walls are 9ft high and 1ft thick. Two of the walls of the house are 40ft long and the others are 30ft long. The house is maintained at 70F° at all times while the temperature of the outdoors varies. On a certain day, the temperature of the inner surface of the walls is measured to be at 55F° while the average temperature of the outer surface is observed to remain at 45F° during the day for 10h and at 35F° at night for 14h. Determine the amount of heat lost from the house that day. Also determine the cost of that heat loss to the homeowner for an electricity price of 0.09$ /kWh.
Answers: 191.520 Btu, 5.05$
3.6- A cylindrical resistor element on a circuit board dissipates 0.15 W of power in an environment at 40C°. The resistor is 1.2cm long, and has a diameter of 0.3cm. Assuming heat to be
transferred uniformly from all surfaces,
determine (a) the amount of heat this resistor
dissipates during a 24-h period, (b) the heat flux on the surface of the resistor, in W/m2, and (c) the surface temperature of the resistor for a combined convection and radiation heat transfer coefficient of 9 W/m2 ·C°.
Answers: 3.6W·h, 1179W/m2, 171C°
3.7- Water is boiling in a 25cm-diameter aluminum pan (k = 237 W/m ·C°) at 95C°. Heat is transferred steadily to the boiling water in the pan through its 0.5cm-thick flat bottom at a rate of 800 W. If the inner surface temperature of the bottom of the pan is 108C°, determine (a) the boiling heat transfer coefficient on the inner surface of the pan, and (b) the outer surface temperature of the bottom of the pan.
Answers: 1254 W/m2 ·C°, 108.3C°
3.8- A wall is constructed of two layers of 0.5in- thick sheetrock (k = 0.10 Btu/h ·ft ·F°), which is
Prob.(3.5)

## Slide 26
Chapter Three
Steady Heat Conduction
3.10- A 2m×1.5m section of wall of an industrial furnace burning natural gas is not insulated, and the temperature at the outer surface of this section is measured to be 80C°. The temperature of the furnace room is 30C°, and the combined convection and radiation heat transfer coefficient at the surface of the outer furnace is 10 W/m2 ·C°. It is proposed to insulate this section of the furnace wall with glass wool insulation (k =0.038 W/m ·C°) in order to reduce the heat loss by 90 percent. Assuming the outer surface temperature of the metal section still remains at about 80C°, determine the thickness of the insulation that
needs to be used. The furnace operates continuously and has an efficiency of 78 percent.
The price of the natural gas is 0.55$/therm (1 therm = 105,500 kJ of energy content). If the installation of the insulation will cost 250$ for materials and labor, determine how long it will take for the insulation to pay for itself from the
energy it saves. Answers: 3.4cm, 0.88year
3.11- Repeat Prob.(3.10) for expanded perlite insulation assuming conductivity is k = 0.052 W/m ·C°. Answers: 4.7cm, 0.88year
3.12- Consider a house whose walls are 12ft-high and 40ft-long. Two of the walls of the house have no windows, while each of the other two walls has four windows made of 0.25in-thick glass (k =
0.45 Btu/h ·ft ·F°), 3ft×5ft in size. The walls are certified to have an R-value of (L/k = 19h ·ft2
F°/Btu). Disregarding any direct radiation gain
or loss through the windows and taking the heat transfer coefficients at the inner and outer surfaces of the house to be 2 and 4 Btu/h ·ft2 ·F°,
respectively, determine the transfer through the walls windows.
ratio of the heat with and without Answer: 17.7
3.13- Consider a house that has a 10m×20m-base and a 4m-high wall. All four walls of the house have an R-value of 2.31m2 ·C°/W. The two 10m×4m-walls have no windows. The third wall
Prob.(3.12)
a plasterboard made of two layers of heavy paper separated by a layer of gypsum, placed 5in-apart. The space between the sheetrocks is filled with fiberglass insulation (k = 0.020 Btu/h ·ft ·F°). Determine the thermal resistance of the wall.
Answer: 21.66ft2 ·F° ·h /Btu
3.9- The roof of a house consists of a 3cm-thick concrete slab (k = 2 W/m ·C°) that is 15m-wide and 20m-long. The convection heat transfer coefficients on the inner and outer surfaces of the roof are 5 and 12 W/m2 ·C°, respectively. On a clear winter night, the ambient air is reported to be at 10C°, while the night sky temperature is 100 K°. The house and the interior surfaces of the wall are maintained at a constant temperature of 20C°. The emissivity of both surfaces of the concrete roof is 0.9. Considering both radiation and convection heat transfers, determine the rate of heat transfer through the roof, and the inner surface temperature of the roof. If the house is heated by a furnace burning natural gas with an efficiency of 80 percent, and the price of natural gas is 0.6$/therm (1 therm=105,500 kJ of energy content), determine the money lost through the roof that night during a 14h period.
Answers: 37440W, 7.3C°, 13.4$
Prob.(3.9)
Prob.(3.8)
66

## Slide 27
Chapter Three
Steady Heat Conduction
has five windows made of 0.5cm-thick glass (k =
0.78 W/m ·C°), 1.2m×1.8m in size. The fourth wall has the same size and number of windows, but they are double-paned with a 1.5cm-thick stagnant air space (k = 0.026 W/m ·C°) enclosed between two 0.5cm-thick glass layers. The thermostat in the house is set at 22C° and the average temperature outside at that location is 8C° during the seven-month-long heating season. Disregarding any direct radiation gain or loss through the windows and taking the heat transfer coefficients at the inner and outer surfaces of the house to be 7 and 15 W/m2 ·C°, respectively, determine the average rate of heat transfer through each wall. If the house is electrically heated and the price of electricity is 0.08$/kWh, determine the amount of money this household will save per heating season by converting the single-pane windows to double-pane windows.
. Answers: 222.3W, 4372W, 600W, 1521$
3.14- The wall of a refrigerator is constructed of
fiberglass insulation (k = 0.035 W/m ·C°) set
between two layers of 1mm-thick sheet metal (k=
15.1 W/m ·C°). The refrigerated space is maintained at 3C°, and the average heat transfer coefficients at the inner and outer surfaces of the wall are 4 and 9 W/m2 ·C°, respectively. The kitchen temperature averages 25C°. It is observed that condensation occurs on the outer surfaces of the refrigerator when the temperature of the outer surface drops to 20C°. Determine the minimum thickness of fiberglass insulation that needs to be used in the wall in order to avoid condensation on
the outer surfaces. Answer: 0.45cm
3.15- Heat is to be conducted along a circuit board that has a copper layer on one side and epoxy layer on other side. The circuit board is 15cm-long and 15cm-wide, and the thicknesses of the copper and epoxy layers are 0.1mm and
Prob.(3.14)
1.2mm, respectively. Disregarding heat transfer from side surfaces, determine the percentages of heat conduction along the copper (k = 386 W/m·C°) and epoxy (k = 0.26 W/m ·C°) layers. Also determine the effective thermal conductivity of the board.
Answers: 99.2%, 0.8%, 29.9 W/m ·C°
3.16- A 0.03in-thick copper plate (k = 223 Btu/h
ft ·F°) is sandwiched between two 0.1in-thick epoxy boards (k = 0.15 Btu/h ·ft ·F°) that are 7in×9in in size. Determine the effective thermal conductivity of the board along its 9in-long side. What fraction of the heat conducted along that side is conducted through copper?
Answers: 29.2 Btu/h ·ft ·F°, 99.6%
3.17- A 4m-high and 6m-wide wall consists of a long 18cm×30cm cross section of horizontal bricks (k = 0.72 W/m ·C°) separated by 3cm- thick plaster layers (k = 0.22 W/m ·C°). There are also 2cm-thick plaster layers on each side of the wall, and a 2cm-thick rigid foam (k =0.026 W/m
C°) on the inner side of the wall. The indoor and the outdoor temperatures are 22C° and -4C°, and the convection heat transfer coefficients on the inner and the outer sides are h1 = 10 W/m2 ·C° and h2 = 20 W/m2 ·C°, respectively. Assuming one-dimensional heat transfer and disregarding radiation, determine the rate of heat transfer through the wall. Answer: 450 W
3.18- A 10in-thick, 30ft-long, and 10ft-high wall is to be constructed using 9in-long solid bricks (k
= 0.4 Btu/h ·ft ·F°) of cross section 7in×7in, or identical size bricks with nine square air holes (k
= 0.015 Btu/h ·ft ·F°) that are 9in-long and have a cross section of 1.5in×1.5in. There is a 0.5in-
thick plaster layer (k =0.10 Btu/h ·ft ·F°) between
Prob.(3.17)

## Slide 28
Chapter Three
Steady Heat Conduction
two adjacent bricks on all four sides and on both sides of the wall. The house is maintained at 80F° and the ambient temperature outside is 30F°. Taking the heat transfer coefficients at the inner and outer surfaces of the wall to be 1.5 and 4 Btu/h ·ft2 ·F°, respectively, determine the rate of heat transfer through the wall constructed of
(a) solid bricks and (b) bricks with air holes.
Answers: 3921 Btu/h, 3275 Btu/h
3.19- Consider a 5m-high, 8m-long, and 0.22m- thick wall whose representative cross section is as given in the figure. The thermal conductivities of various materials used, in W/m ·C°, are kA = kF
= 2, kB = 8, kC = 20, kD = 15 and kE = 35. The
left and right surfaces of the wall are maintained at uniform temperatures of 300C° and 100C°, respectively. Assuming heat transfer through the wall to be one-dimensional, determine (a) the rate of heat transfer through the wall; (b) the temperature at the point where the sections B, D, and E meet; and (c) the temperature drop across the section F. Disregard any contact resistances at the interfaces.
Answers: 1.91×105W, 263C°, 143C°
Prob.(3.19)
Prob.(3.18)
3.20- A 5m-wide, 4m-high, and 40m-long kiln used to cure concrete pipes is made of 20cm- thick concrete walls and ceiling (k =0.9W/m ·C°). The kiln is maintained at 40C° by injecting hot steam into it. The two ends of the kiln, 4m×5m in size, are made of a 3mm-thick sheet metal covered with 2cm-thick Styrofoam (k = 0.033
W/m·C°). The convection heat transfer
coefficients on the inner and the outer surfaces of
the kiln are 3000 and 25 W/m2 ·C°, respectively. Disregarding any heat loss through the floor, determine the rate of heat loss from the kiln when the ambient air is at -4C°.
Answer: 88,000 W
3.21- Consider a 6in×8in epoxy glass laminate (k
= 0.10 Btu/h ·ft ·F°) whose thickness is 0.05in. In order to reduce the thermal resistance across its thickness, cylindrical copper fillings (k = 223 Btu/h ·ft ·F°) of 0.02in diameter are to be planted throughout the board, with a center-to-center distance of 0.06in. Determine the new value of the thermal resistance of the epoxy board for heat conduction across its thickness as a result of this modification.
Answer: 0.00064 h ·F°/Btu
Prob.(3.21)
Prob.(3.20)

## Slide 29
Chapter Three
Steady Heat Conduction
3.22- A 5m-internal-diameter spherical tank made of 1.5cm-thick stainless steel (k = 15 W/m
C°) is used to store iced water at 0C°. The tank is
located in a room whose temperature is 30C°. The walls of the room are also at 30C°. The outer surface of the tank is black (emissivity ε = 1), and heat transfer between the outer surface of the tank and the surroundings is by natural convection and
radiation. The convection heat transfer
coefficients at the inner and the outer surfaces of the tank are 80 and 10 W/m2 ·C°, respectively. Determine (a) the rate of heat transfer to the iced water in the tank and (b) the amount of ice at 0C° that melts during a 24h-period. The heat of fusion of water at atmospheric pressure is hif = 333.7
kJ/kg. Answers: 30,581 W, 7918kg
3.23- Steam at 320C° flows in a stainless steel pipe (k = 15 W/m ·C°) whose inner and outer diameters are 5cm and 5.5cm, respectively. The pipe is covered with 3cm-thick glass wool insulation (k = 0.038 W/m ·C°). Heat is lost to the surroundings at 5C° by natural convection and radiation, with a combined natural convection and radiation heat transfer coefficient of 15 W/m2
C°. Taking the heat transfer coefficient inside the
pipe to be 80W/m2 ·C°, determine the rate of heat loss from the steam per unit length of the pipe. Also determine the temperature drops across the pipe shell and the insulation.
Answers: 93.9 W, 0.095C°, 290C°
3.24- A 50m-long section of a steam pipe whose outer diameter is 10cm passes through an open space at 15C°. The average temperature of the outer surface of the pipe is measured to be 150C°. If the combined heat transfer coefficient on the outer surface of the pipe is 20 W/m2 ·C°, determine (a) the rate of heat loss from the steam pipe, (b) the annual cost of this energy lost if steam is generated in a natural gas furnace that has an efficiency of 75% and the price of natural
Prob.(3.22)
gas is 0.52$/therm (1 therm = 105,500 kJ), and
(c) the thickness of fiberglass insulation (k=0.035 W/m ·C°) needed in order to save 90% of the heat lost. Assume the pipe temperature to remain constant at 150C°.
Answers: 42,412 W, 8790$ /year,1.92cm
3.25- Steam exiting the turbine of a steam power plant at 100F° is to be condensed in a large condenser by cooling water flowing through copper pipes (k = 223 Btu/h ·ft ·F°) of inner diameter 0.4in and outer diameter 0.6in at an average temperature of 70F°. The heat of vaporization of water at 100F° is 1037 Btu/lbm. The heat transfer coefficients are 1500 Btu/h ·ft2
F° on the steam side and 35 Btu/h ·ft2 ·F° on the
Determine the length of the tube condense steam at a rate of 120
water side. required to lbm/h.
Answer: 1148 ft
3.26- Consider a 3m-diameter spherical tank that is initially filled with liquid nitrogen at 1 atm and
-196C°. The tank is exposed to ambient air at
15C°, with a combined convection and radiation heat transfer coefficient of 35 W/m2·C°. The temperature of the thin-shelled spherical tank is
observed to be almost the same as the
temperature of the nitrogen inside. If the heat of vaporization liquid nitrogen at 1 atm is given to
Prob.(3.25)
Prob.(3.24)

## Slide 30
Chapter Three
Steady Heat Conduction
be 198kJ/kg. Determine the rate of evaporation of the liquid nitrogen in the tank as a result of the heat transfer from the ambient air if the tank is
(a) not insulated, (b) insulated with 5cm-thick fiberglass insulation (k = 0.035 W/m ·C°), and (c) insulated with 2cm-thick super-insulation which has an effective thermal conductivity of 0.00005 W/m ·C°.
Answers: 1.055kg/s, 0.0214kg/s, 0.000076kg/s
3.27- A 2mm-diameter and 10m-long electric wire is tightly wrapped with a 1mm-thick plastic cover whose thermal conductivity is k =0.15 W/m
C°. Electrical measurements indicate that a
current of 10A passes through the wire and there is a voltage drop of 8V along the wire. If the insulated wire is exposed to a medium at T∞=30C° with a heat transfer coefficient of h= 24 W/m2 ·C°, determine the temperature at the interface of the wire and the plastic cover in steady operation. Also determine if doubling the thickness of the plastic cover will increase or decrease this interface temperature.
Answer: 62.4 C°, It decrease
3.28- A 0.083in-diameter electrical wire at 115F°
is covered by 0.02in-thick plastic insulation (k =
0.075 Btu/h ·ft ·F°). The wire is exposed to a medium at 50F° with a combined convection and radiation heat transfer coefficient of 2.5 Btu/h ·ft2
F°. Determine if the plastic insulation on the
wire will increase or decrease heat transfer from the wire.
Answer: It helps
Prob.(3.27)
Prob.(3.26)
3.29- A 5mm-diameter spherical ball at 50C° is covered by a 1mm-thick plastic insulation (k =
0.13 W/m ·C°). The ball is exposed to a medium
at 15C°, with a combined convection and radiation heat transfer coefficient of 20W/m2 ·C°. Determine if the plastic insulation on the ball will help or hurt heat transfer from the ball.
Answer: It helps
3.30- Obtain a relation for the fin efficiency for a fin of constant cross-sectional area Ac, perimeter p, length L, and thermal conductivity k exposed to convection to a medium at T∞ with a heat transfer coefficient h. Assume the fins are sufficiently long so that the temperature of the fin at the tip is nearly T∞. Take the temperature of the fin at the base to be Tb and neglect heat transfer from the fin tips. Simplify the relation for
(a) a circular fin of diameter D & (b) rectangular fins of thickness t.
3.31- Steam in a heating system flows through tubes whose outer diameter is 5cm and whose walls are maintained at a temperature of 180C°. Circular aluminum fins (k = 186 W/m ·C°) of outer diameter 6cm and constant thickness 1mm are attached to the tube. The space between the fins is 3mm, and thus there are 250 fins per meter length of the tube. Heat is transferred to the surrounding air at T∞ = 25C°, with a heat transfer coefficient of 40 W/m2 ·C°. Determine the increase in heat transfer from the tube per meter of its length as a result of adding fins.
Answer: 2639 W
Prob.(3.31)
Prob.(3.29)

## Slide 31
Chapter Three
Steady Heat Conduction
3.36- Two 3m-long and 0.4cm-thick cast iron (k
= 52 W/m ·C°) steam pipes of outer diameter 10cm are connected to each other through two 1cm-thick flanges of outer diameter 20cm. The steam flows inside the pipe at an average temperature of 200C° with a heat transfer coefficient of 180 W/m2 ·C°. The outer surface of the pipe is exposed to an ambient at 12C°, with a heat transfer coefficient of 25W/m2·°C. (a) Disregarding the flanges, determine the average outer surface temperature of the pipe. (b) Using this temperature for the base of the flange and treating the flanges as the fins, determine the fin efficiency and the rate of heat transfer from the flanges. (c) What length of pipe is the flange section equivalent to for heat transfer purposes?
Answers: 174.8 C°, 0.88, 214 W, 8.35cm
Prob.(3.36)
3.32- Consider a stainless steel spoon (k = 8.7 Btu/h ·ft ·F°) partially immersed in boiling water at 200F° in a kitchen at 75F°. The handle of the spoon has a cross section of 0.08in×0.5in, and extends 7in in the air from the free surface of the water. If the heat transfer coefficient at the exposed surfaces of the spoon handle is 3 Btu/h
ft2 ·F°, determine the temperature difference across the exposed surface of the spoon handle. State your assumptions.
Answer: 124.6 F°
3.33- Repeat Prob.(3.32) for a silver spoon (k = 247 Btu/h .ft ·F°).
Answer: 55.9 F°
3.34- A hot surface at 100C° is to be cooled by attaching 3cm-long, 0.25cm-diameter aluminum pin fins (k = 237 W/m ·C°) to it, with a center-to- center distance of 0.6cm. The temperature of the surrounding medium is 30C°, and the heat transfer coefficient on the surfaces is 35 W/m2
C°. Determine the rate of heat transfer from the surface for a 1m×1m section of the plate. Also determine the overall effectiveness of the fins.
Answers: 17.4 kW, 7.1
Prob.(3.34)
3.35- Repeat Prob.(3.34) using copper fins (k = 386 W/m ·C°) instead of aluminum ones.
Prob.(3.32)
Answers: 17.8 kW, 7.27