## Slide 1: Fabrication and Processing of Glasses and Glass–Ceramics
CERAMIC- FOURTH CLASS
1 | P a g e
Soda and lime are added to a glass
batch in the form of soda ash (Na2CO3) and limestone (CaCO3). During heating, these two ingredients
decompose to give off carbon dioxide (CO2), the resulting products being soda and lime. Compute the weight of
soda ash and limestone that must be

## Slide 2: added to 125 lbm of quartz (SiO2) to
CERAMIC- FOURTH CLASS
2 | P a g e
yield a glass of composition 78 wt%
SiO2, 17 wt% Na2O, and 5 wt% CaO.
What is the distinction between glass transition temperature and melting temperature?
Compare the temperatures at which soda– lime, borosilicate, 96% silica, and fused silica may be annealed.

## Slide 3
CERAMIC- FOURTH CLASS
Compare the softening points for 96%
silica, borosilicate, and soda–lime glasses.
Explain why residual thermal stresses are introduced into a glass piece when it is cooled.
Are thermal stresses introduced upon heating? Why or why not?
3 | P a g e

## Slide 4
CERAMIC- FOURTH CLASS
Borosilicate glasses and fused silica
are resistant to thermal shock. Why is this so?
In your own words, briefly describe what happens as a glass piece is thermally tempered.
Glass pieces may also be strengthened by chemical tempering. With this procedure, the glass surface is put in a state of compression by exchanging some of the cations near
4 | P a g e

## Slide 5: the surface with other cations having
CERAMIC- FOURTH CLASS
5 | P a g e
a larger diameter. Suggest one type of
cation that, by replacing Na+, will induce chemical tempering in a soda–
Processing
of Clay
lime glass.
Fabrication and Products
Cite the two desirable characteristics
of clay minerals relative to fabrication processes.

## Slide 6
CERAMIC- FOURTH CLASS
From a molecular perspective, briefly
explain the mechanism by which clay minerals become hydroplastic when
water is added.
What are the three main components of a whiteware ceramic such as porcelain?
What role does each component play in the forming and firing procedures?
6 | P a g e

## Slide 7
CERAMIC- FOURTH CLASS
Why is it so important to control the
rate of drying of a ceramic body that has been hydroplastically formed or
slip cast?
Cite three factors that influence the rate of drying, and explain how each affects the rate.
Cite one reason why drying shrinkage is greater for slip cast or hydroplastic products that have smaller clay particles.
7 | P a g e

## Slide 8
CERAMIC- FOURTH CLASS
Name three factors that influence the
degree to which vitrification occurs in claybased ceramic wares.
Explain how density, firing distortion,
strength, corrosion resistance, and thermal conductivity are affected by the extent of vitrification.
8 | P a g e

## Slide 9: Powder Pressing
CERAMIC- FOURTH CLASS
9 | P a g e
Some ceramic materials are
fabricated by hot isostatic pressing. Cite some of the limitations and
difficulties associated with this technique.
DESIGN PROBLEM
modern
kitchen
Some of our
cookware is
made of
ceramic
materials.

## Slide 10
CERAMIC- FOURTH CLASS
List at least three important
characteristics required of a material to be used for this application.
Make a comparison of three ceramic materials as to their relative properties and, in addition, to cost.
On the basis of this comparison, select the material most suitable for the cookware.
Written by Assist. Lec Athil S. Ibrahim
All the best
10 | P a g e