## Slide 1: More Course Details
BOOK – Strength of Materials 4th edition (Solutions Manual) Singer Pytel (Legibly)
COURSE WORK
1. Two Mid-Semester Test (40%);
2. Practical report (10%) and
3. End of Semester 1 Examination (50%).

## Slide 2: MAE207: CHAPTER ONE
STRESS AND STRAIN RELATIONS

## Slide 3: 1.1 DIRECT OR NORMAL STRESS
When a force is transmitted through a body, the body tends to change its shape or deform.The body is said to be strained.
Direct Stress = Applied Force (F)
Cross Sectional Area (A)
Units: Usually N/m2 (Pa), N/mm2, MN/m2, GN/m2 or N/cm2
Note: 1 N/mm2 = 1 MN/m2 = 1 MPa

## Slide 4: Direct Stress Contd.
Direct stress may be tensile, t or compressive,c and result from forces acting perpendicular to the plane of the cross-section
Tension
Compression

## Slide 5: 1.2 Direct or Normal Strain
When loads are applied to a body, some deformation will occur resulting to a change in dimension.
Consider a bar, subjected to axial tensile loading force, F. If the bar extension is dl and its original length (before loading) is L, then tensile strain is:

## Slide 6: Direct or Normal Strain Contd.
Direct Strain ( ) = Change in Length
Original Length
i.e. = dl/L
dl
F
F
L

## Slide 7: Direct or Normal Strain Contd.
As strain is a ratio of lengths, it is dimensionless.
Similarly, for compression by amount, dl: Compressive strain = - dl/L
Note: Strain is positive for an increase in dimension and negative for a reduction in dimension.

## Slide 8: 1.3 Shear Stress and Shear Strain
Shear stresses are produced by equal and opposite parallel forces not in line.
The forces tend to make one part of the material slide over the other part.
Shear stress is tangential to the area over which it acts.

## Slide 9: Shear Stress and Shear Strain Contd.
P
Q
S
R
F
D
D’
A
B
C
C’
L
x
Shear strain is the distortion produced by shear stress on an element or rectangular block as above. The shear strain, (gamma) is given as:
= x/L = tan

## Slide 10: Shear Stress and Shear Strain Concluded
For small ,
Shear strain then becomes the change in the right angle.
It is dimensionless and is measured in radians.