## Slide 1
Chapter 2
THE FIRST LAW OF THERMODYNAMICS
  INTRODUCTION
Kinetic energy is conserved in a frictionless system of interacting rigid elastic bodies. A collision between two of these bodies results in a transfer of kinetic energy from one to the other, the work done by the one equals the work done on the other, and the total kinetic energy of the system is unchanged as a result of the collision. If the kinetic system is in the influence of a gravitational field, then the sum of the kinetic and potential energies of the bodies is constant; changes of position of the bodies in the gravitational field, in addition to changes in the velocities of the bodies, do not alter the total dynamic energy of the system. As the result of possible interactions, kinetic energy may be converted to potential energy and vice versa, but the sum of the two remains constant. If, however, friction occurs in the system, then with continuing collision and interaction among the bodies, the total dynamic energy of the system decreases and heat is produced. It is thus reasonable to expect that a relationship exists between the dynamic energy dissipated and the heat produced as a result of the effects of friction.
The establishment of this relationship laid the foundations for the development of the thermodynamic method. As a subject, this has now gone far beyond simple considerations of the interchange of energy from one form to another, e.g., from dynamic energy to thermal energy. The development of thermodynamics from its early beginnings to its present state was achieved as the result of the invention of convenient thermodynamic functions of state. In this chapter the first two of these thermodynamic functions—the internal energy U and the enthalpy H—are introduced.
  THE RELATIONSHIP BETWEEN HEAT AND WORK
The relation between heat and work was first suggested in 1798 by Count Rumford, who, during the boring of cannon at the Munich Arsenal, noticed that the heat produced during the boring was roughly proportional to the work performed during the boring. This suggestion was novel, as hitherto heat had been regarded as being an invisible fluid called caloric which resided between the constituent particles of a substance. In the caloric theory of heat, the temperature of a substance was considered to be determined by the quantity of caloric gas which it contained, and two bodies of differing temperature, when placed in contact with one another, came to an intermediate common temperature as the result of caloric flowing between them. Thermal equilibrium was reached when the pressure of caloric gas in the one body equaled that in the other. Rumford’s observation that heat production accompanied the performance of work was accounted for by the caloric theory as being due to the fact that the amount of caloric which could be contained by a body, per unit mass of the body, depended on the mass of the body. Small pieces of metal (the metal turnings produced by the boring) contained less caloric per unit mass than did the original large mass of metal, and thus, in reducing the original large

## Slide 2
18 Introduction to the Thermodynamics of Materials
mass to a number of smaller pieces, caloric was evolved as sensible heat. Rumford then demonstrated that when a blunt borer was used (which produced very few metal turnings), the same heat production accompanied the same expenditure of work. The caloric theory “explained” the heat production in this case as being due to the action of air on the metal surfaces during the performance of work.
The caloric theory was finally discredited in 1799 when Humphrey Davy melted two blocks of ice by rubbing them together in a vacuum. In this experiment the latent heat necessary to melt the ice was provided by the mechanical work performed in rubbing the blocks together.
From 1840 onwards the relationship between heat and work was placed on a firm quantitative basis as the result of a series of experiments carried out by James Joule. Joule conducted experiments in which work was performed in a certain quantity of adiabatically* contained water and measured the resultant increase in the temperature of the water. He observed that a direct proportionality existed between the work done and the resultant increase in temperature and that the same proportionality existed no matter what means were employed in the work production. Methods of work production used by Joule included
Rotating a paddle wheel immersed in the water
An electric motor driving a current through a coil immersed in the water
Compressing a cylinder of gas immersed in the water
Rubbing together two metal blocks immersed in the water
This proportionality gave rise to the notion of a mechanical equivalent of heat, and for the purpose of defining this figure it was necessary to define a unit of heat. This unit is the calorie (or 15° calorie), which is the quantity of heat required to increase the temperature of 1 gram of water from 14.5°C to 15.5°C. On the basis of this definition Joule determined the value of the mechanical equivalent of heat to be 0.241 calories per joule. The presently accepted value is 0.2389 calories (15° calories) per joule. Rounding this to
0.239 calories per joule defines the thermochemical calorie, which, until the introduction in 1960 of S.I. units, was the traditional energy unit used in thermochemistry.
2.3 INTERNAL ENERGY AND THE FIRST LAW OF THERMODYNAMICS
Joule’s experiments resulted in the statement that “the change of a body inside an adiabatic enclosure from a given initial state to a given final state involves the same
*An adiabatic vessel is one which is constructed in such a way as to prohibit, or at least minimize, the passage of heat through its walls. The most familiar example of an adiabatic vessel is the Dewar flask (known more popularly as a thermos flask). Heat transmission by conduction into or out of this vessel is minimized by using double glass walls separated by an evacuated space, and a rubber or cork stopper, and heat transmission by radiation is minimized by using highly polished mirror surfaces.

## Slide 3
The First Law of Thermodynamics 19
amount of work by whatever means the process is carried out.” The statement is a prelim- inary formulation of the First Law of Thermodynamics, and in view of this state- ment, it is necessary to define some function which depends only on the internal state of a body or system. Such a function is U, the internal energy. This function is best introduced by means of comparison with more familiar concepts. When a body of mass m is lifted in a gravitational field from height h1 to height h2, the work w done on the body is given by
As the potential energy of the body of given mass m depends only on the position of the body in the gravitational field, it is seen that the work done on the body is dependent only on its final and initial positions and is independent of the path taken by the body between the two positions, i.e., between the two states. Similarly the application of a force f to a body of mass m causes the body to accelerate according to Newton’s Law
where a=dv/dt, the acceleration.
The work done on the body is thus obtained by integrating
where l is distance.
Integration gives
Thus, again, the work done on the body is the difference between the values of a function of the state of the body and is independent of the path taken by the body between the states.

## Slide 4
If work w is done on the body, then UB>UA and if the body itself performs work, then
UB<UA.
In Joule’s experiments the change in the state of the adiabatically contained water was measured as an increase in the temperatures of the water. The same increase in temperature, and hence the same change of state, could have been produced by placing the water in thermal contact with a source of heat and allowing heat q to flow into the water. In describing heat changes it is conventional to assign a negative value to heat which flows out of a body (an exothermic process) and a positive value to heat which flows into a body (an endothermic process). Hence,
Thus, when heat flows into the body, q is a positive quantity and UB>UA, whereas if heat flows out of the body, UB<UA and q is a negative quantity.
It is now of interest to consider the change in the internal energy of a body which simultaneously performs work and absorbs heat. Consider a body, initially in the state A, which performs work w, absorbs heat q, and, as a consequence, moves to the state B. The absorption of heat q increases the internal energy of the body by the amount q, and the performance of work w by the body decreases its internal energy by the amount w. Thus the total change in the internal energy of the body, OU, is
(2.1)
This is a statement of the First Law of Thermodynamics.
For an infinitesimal change of state, Eq. (2.1) can be written as a differential
(2.2)
20 Introduction to the Thermodynamics of Materials
In the case of work being done on an adiabatically contained body of constant potential and kinetic energy, the pertinent function which describes the state of the body, or the change in the state of the body, is the internal energy U. Thus the work done on, or by, an adiabatically contained body equals the change in the internal energy of the body, i.e., equals the difference between the value of U in the final state and the value of U in the initial state. In describing work, it is conventional to assign a negative value to work done on a body and a positive value to work done by a body. This convention arises because, when a gas expands, and hence does work against an external pressure, the integral
, which is the work performed, is a positive quantity. Thus for an adiabatic process in which work w is done on a body, as a result of which its state moves from A to B.

## Slide 5
The vanishing of a cyclic integral is a property of a state function.
In Joule’s experiments, where (U2–U1)=–w, the process was adiabatic (q=0), and thus
the path of the process was specified.
The First Law of Thermodynamics 21
Notice that the left-hand side of Eq. (2.2) gives the value of the increment in an already existing property of the system, whereas the right-hand side has no corresponding interpretation. As U is a state function, the integration of dU between two states gives a value which is independent of the path taken by the system between the two states. Such is not the case when 6q and 6w are integrated. The heat and work effects, which involve energy in transit, depend on the path taken between the two states, as a result of which the integrals of 6w and 6q cannot be evaluated without a knowledge of the path. This is illustrated in Fig. 2.1. In Fig. 2.1 the value of U2–U1 is independent of the path taken
between state 1 (P1V1) and state 2 (P2V2). However, the work done by the system, which
is given by the integral and hence is the area under the curve between V2 and V1, can vary greatly depending on the path. In Fig. 2.1 the work done in the process 1 → 2 via c is less than that done via b which, in turn, is less than that done via a.
From Eq. (2.1) it is seen that the integral of 6q must also depend on the path, and in the process 1 → 2 more heat is absorbed by the system via a than is absorbed via b which, again in turn, is greater than the heat absorbed via c. In Eq. (2.2) use of the symbol “d” indicates a differential element of a state function or state property, the integral of which is independent of the path, and use of the symbol “6” indicates a differential element of some quantity which is not a state function. In Eq. (2.1) note that the algebraic sum of two quantities, neither of which individually is independent of the path, gives a quantity which is independent of the path.
In the case of a cyclic process which returns the system to its initial state, e.g., the process 1 → 2 → 1 in Fig. 2.1, the change in U as a result of this process is zero; i.e.,

## Slide 6
22 Introduction to the Thermodynamics of Materials
Figure 2.1 Three process paths taken by a fixed quality of gas in moving from the state 1 to the state 2.
As U is a state function, then for a simple system consisting of a given amount of substance of fixed composition, the value of U is fixed once any two properties (the independent variables) are fixed. If temperature and volume are chosen as the independent variables, then
The complete differential U in terms of the partial derivatives gives
As the state of the system is fixed when the two independent variables are fixed, it is of interest to examine those processes which can occur when the value of one of the independent variables is maintained constant and the other is allowed to vary. In this manner we can examine processes in which the volume V is maintained constant (isochore or isometric processes), or the pressure P is maintained constant (isobaric

## Slide 7
The First Law of Thermodynamics 23
processes), or the temperature T is maintained constant (isothermal processes). We can also examine adiabatic processes in which q=0.
2.4 CONSTANT-VOLUME PROCESSES
If the volume of a system is maintained constant during a process, then the system does no work (∫PdV=0), and from the First Law, Eq. (2.2),
(2.3)
where the subscript v indicates constant volume. Integration of Eq. (2.3) gives
for such a process, which shows that the increase or decrease in the internal energy of the sys- tem equals, respectively, the heat absorbed or rejected by the system during the process.
2.5 CONSTANT-PRESSURE PROCESSES AND THE ENTHALPY H
If the pressure is maintained constant during a process which takes the system from state 1 to state 2, then the work done by the system is given as
and the First Law gives
where the subscript p indicates constant pressure. Rearrangement gives
and, as the expression (U+PV) contains only state functions, the expression itself is a state function. This is termed the enthalpy, H; i.e.,
(2.4)
Hence, for a constant-pressure process,

## Slide 8
24 Introduction to the Thermodynamics of Materials
(2.5)
Thus the enthalpy change during a constant-pressure process is equal to the heat admitted to or withdrawn from the system during the process.
2.6 HEAT CAPACITY
Before discussing isothermal and adiabatic processes, it is convenient to introduce the concept of heat capacity. The heat capacity, C, of a system is the ratio of the heat added to or withdrawn from the system to the resultant change in the temperature of the system. Thus
or if the temperature change is made vanishingly small, then
The concept of heat capacity is only used when the addition of heat to or withdrawal of heat from the system produces a temperature change; the concept is not used when a phase change is involved. For example, if the system is a mixture of ice and water at 1 atm pressure and 0°C, then the addition of heat simply melts some of the ice and no change in temperature occurs. In such a case the heat capacity, as defined, would be infinite.
Note that if a system is in a state 1 and the absorption of a certain quantity of heat by the system increases its temperature from T1 to T2, then the statement that the final
temperature is T2 is insufficient to determine the final state of the system. This is because
the system has two independent variables, and so one other variable, in addition to the temperature, must be specified in order to define the state of the system. This second independent variable could be varied in a specified manner or could be maintained constant during the change. The latter possibility is the more practical, and so the addition of heat to a system to produce a change in temperature is normally considered at constant pressure or at constant volume. In this way the path of the process is specified, and the final state of the system is known.
Thus a heat capacity at constant volume, Cv, and a heat capacity at constant pressure,
Cp, are defined as

## Slide 9
The First Law of Thermodynamics 25
Thus, from Eqs. (2.3) and (2.5)
(2.6)
(2.7)
The heat capacity, being dependent on the size of the system, is an extensive property. However, in normal usage it is more convenient to use the heat capacity per unit quantity of the system. Thus the specific heat of the system is the heat capacity per gram at constant P, and the molar heat capacity is the heat capacity per mole at constant pressure or at constant volume. Thus, for a system containing n moles,
and
where Cp and Cv are the molar values.
It is to be expected that, for any substance, Cp will be of greater magnitude than Cv. If
it is required that the temperature of a system be increased by a certain amount, then, if the process is carried out at a constant volume, all of the heat added is used solely to raise the temperature of the system. However, if the process is carried out at constant pressure, then, in addition to raising the temperature by the required amount, the heat added is required to provide the work necessary to expand the system at the constant pressure. This work of expansion against the constant pressure per degree of temperature increase is calculated as

## Slide 10
26 Introduction to the Thermodynamics of Materials
and hence it might be expected that
The difference between Cp and Cv is calculated as follows:
and
Hence
but
and therefore
Hence,
(2.8)

## Slide 11
The First Law of Thermodynamics 27
The two expressions for Cp–Cv differ by the term (6V/6T)P×(6U/6V)T, and in an attempt to evaluate the term (6U/6V)T for gases, Joule performed an experiment which involved
filling a copper vessel with a gas at some pressure and connecting this vessel via a stopcock to a similar but evacuated vessel. The two-vessel system was immersed in a quantity of adiabatically contained water and the stopcock was opened, thus allowing free expansion of the gas into the evacuated vessel. After this expansion, Joule could not detect any change in the temperature of the system. As the system was adiabatically contained and no work was performed, then from the First Law,
and hence
Thus as dT=0 (experimentally determined) and dV=0 then the term (6U/6V)T must be
zero. Joule thus concluded that the internal energy of a gas is a function only of temperature and is independent of the volume (and hence pressure). Consequently, for a gas
However, in a more critical experiment performed by Joule and Thomson, in which an adiabatically contained gas of molar volume V1 at the pressure P1 was throttled through a
porous diaphragm to the pressure P2 and the molar volume V2, a change in the temperature of the gas was observed, which showed that, for real gases, (6U/6V)TÇ0.
Nevertheless, if
then, from Eq. (2.8),

## Slide 12
28 Introduction to the Thermodynamics of Materials
and as, for one mole of ideal gas, PV=RT, then
The reason for Joule’s not observing a temperature rise in the original experiment was that the heat capacity of the copper vessels and the water was considerably greater than the heat capacity of the gas, and thus the small heat changes which actually occurred in the gas were absorbed in the copper vessels and the water. This decreased the actual temperature change to below the limits of the then-available means of temperature measurement.
In Eq. (2.8) the term
represents the work done by the system per degree rise in temperature in expanding against the constant external pressure P acting on the system. The other term in Eq. (2.8), namely,
represents the work done per degree rise in temperature in expanding against the internal cohesive forces acting between the constituent particles of the substance. As will be seen in Chap. 8, an ideal gas is a gas consisting of noninteracting particles, and hence the atoms of an ideal gas can be separated from one another without the expenditure of work. Thus for an ideal gas the above term, and so the term
are zero.
In real gases the internal pressure contribution is very much smaller in magnitude than the external pressure contribution; but in liquids and solids, in which the interatomic forces are considerable, the work done in expanding the system against the external pressure is insignificant in comparison with the work done against the internal pressure. Thus for liquids and solids the term

## Slide 13
The First Law of Thermodynamics 29
is very large.
2.7 REVERSIBLE ADIABATIC PROCESSES
During a reversible process during which the state of the gas is changed, the state of the gas never leaves the equilibrium surface shown in Fig. 1.1. Consequently, during a reversible process, the gas passes through a continuum of equilibrium states, and the
work w is given by the integral only if the process is conducted reversibly. In an adiabatic process q=0, and thus, from the First Law, dU=–6w. Consider a system comprising one mole of an ideal gas. From Eq. (2.6)
and, for a reversible adiabatic process
Thus
As the system is one mole of ideal gas, then P=RT/V and hence
Integrating between states 1 and 2 gives

## Slide 14
or
For an ideal gas it has been shown that Cp–Cv=R. Thus Cp/Cv–1=R/Cv; and if Cp/Cv=μ, then R/Cv=μ–1, and hence
From the ideal gas law,
Thus
and hence
(2.9)
30 Introduction to the Thermodynamics of Materials
or
This is the relationship between the pressure and the volume of an ideal gas under-going a reversible adiabatic process.
2.8 REVERSIBLE ISOTHERMAL PRESSURE OR VOLUME CHANGES OF AN IDEAL GAS
From the First Law

## Slide 15
The First Law of Thermodynamics 31
and as dT=0 (isothermal process), then dU=0. Therefore ðw=ðq=PdV= RTdV/V per mole of gas.
Integrating between the states 1 and 2 gives
(2.10)
hus, for an ideal gas, an isothermal process is one of constant internal energy during which the work done by the system equals the heat absorbed by the system, both of which are given by Eq. (2.10).
A reversible isothermal process and a reversible adiabatic process are shown on a P-V
iagram in Fig. 2.2 in which it is seen that, for a given decrease in pressure, the work
Figure 2.2 Comparison of the process path taken by a reversible isothermal expansion of an ideal gas with the process path taken by a reversible adiabatic expansion of an ideal gas between an initial pressure of 20 atm and a final pressure of 4 atm.

## Slide 16
32 Introduction to the Thermodynamics of Materials
done by the reversible isothermal process (which is equal to the area under the curve) exceeds that done by the reversible adiabatic process. This difference is due to the fact that during the isothermal process heat is absorbed by the system in order to maintain the temperature constant, whereas during the adiabatic process no heat is admitted to the system. During the isothermal expansion the internal energy of the gas remains constant, and during the adiabatic expansion the internal energy decreases by an amount equal to the work done.
2.9 SUMMARY
The establishment of the relationship between the work done on or by a system and the heat entering or leaving the system was facilitated by the introduction of the thermodynamic function U, the internal energy. U is a function of state, and thus the difference between the values of U in two states depends only on the states and is independent of the process path taken by the system in moving between the states. The relationship between the internal energy change, the work done, and the heat absorbed per mole by a system of fixed composition in moving from one state to another is given as OU=q–w, or, for an increment of this process, dU=6q–6w. This relationship is called the First Law of Thermodynamics.
The integrals of 6q and 6w can only be obtained if the process path taken by the system in moving from one state to another is known. Process paths which are convenient for consideration include
  Constant-volume processes in which ∫ðw=∫PdV=0
  Constant-pressure processes in which ∫ðw=P∫dV=POV
  Constant-temperature processes
  Adiabatic processes in which q=0
For a constant-volume process, as w=0, then OU=qv. The definition of the constant- volume molar heat capacity as CV=(6q/dT)V=(6U/6T)V (which is an experimentally measurable quantity) facilitates determination of the change in U resulting from a constant-volume process as
Consideration of constant-pressure processes is facilitated by the introduction of the thermodynamic function H, the enthalpy, defined as H=U+PV. As the expression for H contains only functions of state, then H is a function of state, and thus the difference between the values of H in two states depends only on the states and is independent of the path taken by the system in moving between them. For a constant-pressure process, OH=OU+POV=(qp–POV)+POV=qp. The definition of the constant-pressure
molar heat capacity as Cp=(Oq/dT)P= (6H/6T)P (which is an experimentally measurable quantity) facilitates determination of the change in H as the result of a
constant-pressure process as
.

## Slide 17
8. Only the differences in the values of U and H between two states, i.e., the values of OU and OH, can be measured. The absolute values of U and H in any given state cannot be determined.
2.10 NUMERICAL EXAMPLES
Ten liters of a monatomic ideal gas at 25°C and 10 atm pressure are expanded to a final pressure of 1 atm. The molar heat capacity of the gas at constant volume, Cv, is 3/2 R and
is independent of temperature. Calculate the work done, the heat absorbed, and the change in U and in H for the gas if the process is carried out (1) isothermally and reversibly, and (2) adiabatically and reversibly. Having determined the final state of the gas after the reversible adiabatic expansion, verify that the change in U for the process is independent of the path taken between the initial and final states by considering the process to be carried out as
An isothermal process followed by a constant-volume process
A constant-volume process followed by an isothermal process
An isothermal process followed by a constant-pressure process
A constant-volume process followed by a constant-pressure process
A constant-pressure process followed by a constant-volume process
The size of the system must first be calculated. From consideration of the initial state of the system (the point a in Fig. 2.3)
(a) The isothermal reversible expansion. The state of the gas moves from a to b along the 298 degrees isotherm. As, along any isotherm, the product PV is constant,
The First Law of Thermodynamics 33
For an ideal gas, the internal energy U is a function only of temperature, and
Cp–Cv=R.
The process path of an ideal gas undergoing a reversible adiabatic change of state is described by PVμ=constant, where μ=C /C . During an adiabatic expansion, as q=0,
p v
the decrease in the internal energy of the system equals the work done by the system.
As the internal energy of an ideal gas is a function only of temperature, the internal energy of an ideal gas remains constant during an isothermal change of state. Thus the heat which enters or leaves the gas as a result of the isothermal process equals the work done by or on the gas, with both quantities being given by

## Slide 18
34 Introduction to the Thermodynamics of Materials
Figure 2.3 The five process paths considered in the numerical example.
For an ideal gas undergoing an isothermal process, OU=0 and hence, from the First Law,
Thus in passing from the state a to the state b along the 298 degree isotherm, the system performs 23.3 kilojoules of work and absorbs 23.3 kilojoules of heat from the constant- temperature surroundings.

## Slide 19
(b) The reversible adiabatic expansion. If the adiabatic expansion is carried out reversibly, then during the process the state of the system is, at all time, given by
PVμ=constant, and the final state is the point c in the diagram. The volume V is obtained
C
from as
and
The point c thus lies on the 119 degree isotherm. As the process is adiabatic, q=0 and hence
The work done by the system as a result of the process equals the decrease in the internal energy of the system=9.13 kilojoules.
(i) An isothermal process followed by a constant-volume process (the path a → e → c; that is, an isothermal change from a to e, followed by a constant-volume change from e to c).
and as the state e lies on the 298 degree isotherm then
The First Law of Thermodynamics 35
As, for an ideal gas, H is a function only of temperature, then OH(asb)=0; that is,

## Slide 20
(ii) A constant-volume process followed by an isothermal process (the path a → d → c; that is, a constant-volume change from a to d, followed by an isothermal change from d to c).
(iii) An isothermal process followed by a constant-pressure process (the path a → b → c; that is, an isothermal change from a to b, followed by a constant-pressure change from b to c).
As Cv=1.5 R and Cp–Cv=R, then Cp=2.5 R; and as 1 liter atm equals 101.3 joules,
Thus
(iv) A constant-volume process followed by a constant-pressure process (the path a → f → c; that is, a constant-volume change from a to f, followed by a constant-pressure change from f to c).
36 Introduction to the Thermodynamics of Materials
Thus

## Slide 21
The First Law of Thermodynamics 37
From the ideal gas law
i.e., the state f lies on the 30 degrees isotherm. Thus
Thus
(v) A constant-pressure process followed by a constant-volume process (the path a → g → c; i.e., a constant-pressure step from a to g, followed by a constant-volume step from g to c).
From the ideal gas law
and hence the state g lies on the 1186 degrees isotherm. Thus
Thus

## Slide 22
38 Introduction to the Thermodynamics of Materials
The value of OU(asc) is thus seen to be independent of the path taken by the process between the states a and c.
The change in enthalpy from a to c. The enthalpy change is most simply calculated from consideration of a path which involves an isothermal portion over which OH=0 and an isobaric portion over which OH=qp=∫ncpdT. For example, consider the path a → b → c
and hence
or alternatively
in each of the paths (i) to (v) the heat and work effects differ, although in each case the difference q–w equals –9.12 kilojoules. In the case of the reversible adiabatic path, q=0 and hence w=+9.12 kilojoules. If the processes (i) to (v) are carried out reversibly, then
For path (i) q=–9.12+the area aeih
For path (ii) q=–9.12+the area dcih
For path (iii) q=–9.12+the area abjh–the area cbji
For path (iv) q=–9.12+the area fcih
For path (v) q=–9.12+the area agih
PROBLEMS
  An ideal gas at 300 K has a volume of 15 liters at a pressure of 15 atm. Calculate (1) the final volume of the system, (2) the work done by the system, (3) the heat entering or leaving the system, (4) the change in the internal energy, and (5) the change in the enthalpy when the gas undergoes
    A reversible isothermal expansion to a pressure of 10 atm
    A reversible adiabatic expansion to a pressure of 10 atm
The constant volume molar heat capacity of the gas, Cv, has the value 1.5 R.
  One mole of a monatomic ideal gas, in the initial state T=273 K, P=1 atm, is subjected to the following three processes, each of which is conducted reversibly:

## Slide 23
The First Law of Thermodynamics 39
A doubling of its volume at constant pressure,
Then a doubling of its pressure at constant volume,
Then a return to the initial state along the path P=6.643×10–4V2+ 0.6667.
Calculate the heat and work effects which occur during each of the three processes.
  The initial state of a quantity of monatomic ideal gas is P=1 atm, V=1 liter, and T=373 K. The gas is isothermally expanded to a volume of 2 liters and is then cooled at constant pressure to the volume V. This volume is such that a reversible adiabatic compression to a pressure of 1 atm returns the system to its initial state. All of the changes of state are conducted reversibly. Calculate the value of V and the total work done on or by the gas.
  Two moles of a monatomic ideal gas are contained at a pressure of 1 atm and a temperature of 300 K. 34,166 joules of heat are transferred to the gas, as a result of which the gas expands and does 1216 joules of work against its surroundings. The process is reversible. Calculate the final temperature of the gas.
  One mole of N2 gas is contained at 273 K and a pressure of 1 atm. The addition of
3000 joules of heat to the gas at constant pressure causes 832 joules of work to be done during the expansion. Calculate (a) the final state of the gas, (b) the values of OU and OH for the change of state, and (c) the values of Cv and Cp for N2. Assume that
nitrogen behaves as an ideal gas, and that the above change of state is conducted reversibly.
  Ten moles of ideal gas, in the initial state P1=10 atm, T1=300 K, are taken round the
following cycle:
A reversible change of state along a straight line path on the P–V diagram to the state
P=1 atm, T=300 K,
A reversible isobaric compression to V=24.6 liters, and
A reversible constant volume process to P=10 atm.
How much work is done on or by the system during the cycle? Is this work done on the system or by the system?
  One mole of an ideal gas at 25°C and 1 atm undergoes the following reversibly conducted cycle:
    An isothermal expansion to 0.5 atm, followed by
    An isobaric expansion to 100°C, followed by
    An isothermal compression to 1 atm, followed by
    An isobaric compression to 25°C.
The system then undergoes the following reversible cyclic process.
An isobaric expansion to 100°C, followed by
A decrease in pressure at constant volume to the pressure P atm, followed by
An isobaric compression at P atm to 24.5 liters, followed by
An increase in pressure at constant volume to 1 atm.
Calculate the value of P which makes the work done on the gas during the first cycle equal to the work done by the gas during the second cycle.

## Slide 24
40 Introduction to the Thermodynamics of Materials
2.8 Two moles of an ideal gas, in an initial state P=10 atm, V=5 liters, are taken reversibly in a clockwise direction around a circular path give by (V–10)2
(P–10)2=25. Calculate the amount of work done by the gas as a result of the proces and calculate the maximum and minimum temperatures attained by the gas during th cycle.