## Slide 1
1

## Slide 2
2
2-9 Series Resistors and Voltage Division
The need to combine resistors in series or in parallel occurs so frequently
that it warrants special attention. The process of combining the resistors is facilitated by combining two of them at a time. With this in mind, consider the single-loop circuit of Fig. 1. The two resistors are in series, since the same current 𝑖 flows in both of them.
Fig. 1 A single-loop circuit with two resistors in series.
Applying Ohm’s law to each of the resistors, we obtain
𝑣1 = 𝑖𝑅1, 𝑣2 = 𝑖𝑅2 (1)
If we apply KVL to the loop (moving in the clockwise direction), we have
−𝑣 + 𝑣1 + 𝑣2 = 0
(2)
Combining Eqs. (1) and (2), we get
𝑣 = 𝑣1 + 𝑣2 = 𝑖(𝑅1 + 𝑅2)
(3)
Or
𝑣
𝑖 = 𝑅
1
+ 𝑅
2
(4)

## Slide 3
3
Notice that Eq. (3) can be written as
𝑣 = 𝑖𝑅𝑒𝑞 (5)
implying that the two resistors can be replaced by an equivalent resistor
𝑅𝑒𝑞 ; that is,
𝑅𝑒𝑞 = 𝑅1 + 𝑅2 (6)
Thus, Fig. 1 can be replaced by the equivalent circuit in Fig. 2. The two
circuits in Figs. 1 and 2 are equivalent because they exhibit the same voltage-current relationships at the terminals a-b. An equivalent circuit such as the one in Fig. 2 is useful in simplifying the analysis of a circuit.
Fig. 2 Equivalent circuit of the Fig. 1 circuit
In general,
The equivalent resistance of any number of resistors connected in series is the sum of the individual resistances.
For N resistors in series then,
𝑁
𝑅𝑒𝑞 = 𝑅1 + 𝑅2 + ⋯ + 𝑅𝑁 = ∑ 𝑅𝑛
𝑛=1
(7)
To determine the voltage across each resistor in Fig. 1, we substitute Eq.
(3) into Eq. (1) and obtain
1
𝑣 =
𝑅1
𝑅 + 𝑅 𝑣,
1 2
𝑣2 = 𝑅
𝑅2
+ 𝑅
1 2
𝑣 (8)
Notice that the source voltage 𝑣 is divided among the resistors in direct proportion to their resistances; the larger the resistance, the larger the

## Slide 4
4
voltage drop. This is called the principle of voltage division, and the circuit in Fig. 1 is called a voltage divider. In general, if a voltage divider has N resistors (𝑅1, 𝑅2, … , 𝑅𝑁) in series with the source voltage 𝑣, the nth resistor (𝑅𝑛 ) will have a voltage drop of
𝑛
𝑣 =
𝑅𝑛
𝑅1 + 𝑅2 + ⋯ + 𝑅𝑁
𝑣 (9)
2-10 Parallel Resistors and Current Division
Consider the circuit in Fig. 3, where two resistors are connected in parallel and therefore have the same voltage across them.
Fig. 3 Two resistors in parallel.
From Ohm’s law,
𝑣 = 𝑖1𝑅1 = 𝑖2𝑅2
Or
1
𝑣
𝑅
𝑖 = ,
2
𝑖 =
𝑣
𝑅
1 2
(10)
Applying KCL at node a gives the total current 𝑖 as
𝑖 = 𝑖1 + 𝑖1
(11)
Substituting Eq. (10) into Eq. (11), we get
1
2
1
2
𝑣 𝑣 1 1 𝑣
𝑖 = 𝑅 + 𝑅 = 𝑣 (𝑅 + 𝑅 ) = 𝑅
𝑒𝑞
(12)

## Slide 5
5
Where 𝑅𝑒𝑞 is the equivalent resistance of the resistors in parallel:
𝑅
𝑒𝑞
1
1 1 1
= 𝑅 + 𝑅
2
(13)
Or
𝑅𝑒𝑞
1 𝑅1 + 𝑅2
=
𝑅1𝑅2
Or
𝑒𝑞
𝑅 =
𝑅1𝑅2
𝑅1 + 𝑅2
(14)
Thus,
The equivalent resistance of two parallel resistors is equal to the product of their resistances divided by their sum.
It must be emphasized that this applies only to two resistors in parallel. From Eq. (14), if 𝑅1 = 𝑅2, then 𝑅𝑒𝑞 = 𝑅1⁄2.
We can extend the result in Eq. (13) to the general case of a circuit with N
resistors in parallel. The equivalent resistance is
𝑅
1 1 1
1
𝑒𝑞 1 2 𝑁
= 𝑅 + 𝑅 + ⋯ + 𝑅 (15)
Note that 𝑅𝑒𝑞 is always smaller than the resistance of the smallest resistor in the parallel combination. If 𝑅1 = 𝑅2 = ⋯ = 𝑅𝑁 = 𝑅, 𝑡ℎ𝑒𝑛
𝑅
𝑅𝑒𝑞 = 𝑁 (16)
For example, if four 100- resistors are connected in parallel, their equivalent resistance is 25 .

## Slide 6
6
It is often more convenient to use conductance rather than resistance when dealing with resistors in parallel. From Eq. (15), the equivalent conductance for N resistors in parallel is
𝐺𝑒𝑞 = 𝐺1 + 𝐺2 + 𝐺3 + ⋯ + 𝐺𝑁 (17)
The equivalent conductance of resistors connected in parallel is the sum of their individual conductances.
Thus the equivalent conductance 𝐺𝑒𝑞 of N resistors in series (such as shown in Fig. 1) is
1 1 1 1 1
𝐺
𝑒𝑞 1 2 3 𝑁
= 𝐺 + 𝐺 + 𝐺 + ⋯ + 𝑅 (18)
Given the total current 𝑖 entering node a in Fig. 4, how do we obtain current 𝑖1 and 𝑖2? We know that the equivalent resistor has the same voltage, or
Fig. 4
𝑒𝑞
𝑣 = 𝑖𝑅 =
𝑖𝑅1𝑅2
𝑅1 + 𝑅2
(19)
Combining Eqs. (10) and (18) results in
1
𝑖 =
𝑅2𝑖
𝑅 + 𝑅 ,
1 2
2
𝑅1𝑖
𝑖 =
𝑅 + 𝑅
1 2
(20)

## Slide 7
7
Example 1: Find 𝑅𝑒𝑞 for the circuit shown in Fig. 5.
Fig. 5
Example 2: Find 𝑅𝑒𝑞 for the circuit shown in Fig. 6.
Fig. 6
Example 3: Find 𝑅𝑒𝑞 for the circuit shown in Fig. 7.
Fig. 7

## Slide 8
8
Example 4: Find 𝑅𝑎𝑏 for the circuit shown in Fig. 8.
Fig. 8
Example 5: Find 𝐺𝑒𝑞 for the circuit shown in Fig. 9.
Fig. 9
Example 6: Find 𝐺𝑒𝑞 for the circuit shown in Fig. 10.
Fig. 10

## Slide 9
9
Example 7: Find 𝒊𝒐 and 𝒗𝒐 in the circuit shown if Fig. 11. Calculate the power dissipated in the 3 resistor.
Fig. 11
Example 8: Find 𝒗𝟏 and 𝒗𝟐 in the circuit shown if Fig. 12. Also Calculate 𝒊𝟏 and 𝒊𝟐 and the power dissipated in the 12- and 40- resistors.
Fig. 12
Example 9: For the circuit shown in Fig. 13, determine: (a) the voltage
𝒗𝒐, (b) the power supplied by the current source, (c) the power absorbed by each resistor.
Fig. 13

## Slide 10
10
Example 10: For the circuit shown in Fig. 14, find: (a) 𝒗𝟏 𝒂𝒏𝒅 𝒗𝟐 , (b) the power dissipated in the 3-k, resistors and (c) the power supplied by the current source.