## Slide 1
1

## Slide 2
2
2-13 Wye-Delta Transformations
Situations often arise in circuit analysis when the resistors are neither in parallel nor in series. For example, consider the bridge circuit in Fig. 1.
How do we combine resistors 𝑅1and 𝑅6 through when the resistors are neither in series nor in parallel? Many circuits of the type shown in Fig. 1
Fig. 1
Can be simplified by using three-terminal equivalent networks. These are
the wye (Y) or tee (T) network shown in Fig. 2 and the delta (∆) or pi (Π) network shown in Fig. 3. These networks occur by themselves or as part of a larger network. They are used in three-phase networks, electrical filters, and matching networks. Our main interest here is in how to identify them when they occur as part of a network and how to apply wye-delta transformation in the analysis of that network.
Fig. 2
Two Forms of the same network: (a) Y, (b) T.

## Slide 3
3
Fig. 3
Two Forms of the same network: (a) ∆, (b) Π.
Delta to Wye Conversion
Suppose it is more convenient to work with a wye network in a place
where the circuit contains a delta configuration. We superimpose a wye network on the existing delta network and find the equivalent resistances in the wye network. To obtain the equivalent resistances in the wye network, we compare the two networks and make sure that the resistance between each pair of nodes in the ∆ (or Π) network is the same as the resistance between the same pair of nodes in the Y (or T) network. For terminals 1 and 2 in Figs. 2 and 3, for example,
(1)
𝑅12(𝑌) = 𝑅1 + 𝑅3
𝑅12(∆) = 𝑅𝑏‖(𝑅𝑎 + 𝑅𝑐)
Setting 𝑅12(𝑌) = 𝑅12(∆) gives
𝑅12 = 𝑅1 + 𝑅3
𝑅𝑏(𝑅𝑎 + 𝑅𝑐)
=
𝑅𝑎 + 𝑅𝑏 + 𝑅𝑐
(2𝑎)
Similarly,
13
𝑅 = 𝑅1 + 𝑅2
𝑅𝑐(𝑅𝑎 + 𝑅𝑏)
=
𝑅𝑎 + 𝑅𝑏 + 𝑅𝑐
(2𝑏)
34
𝑅 = 𝑅2 + 𝑅3
𝑅𝑎(𝑅𝑏 + 𝑅𝑐)
=
𝑅𝑎 + 𝑅𝑏 + 𝑅𝑐
(2𝑐)

## Slide 4
4
Subtracting Eq. (2c) from Eq. (2a), we get
𝑅1 − 𝑅2
𝑅𝑐(𝑅𝑏 − 𝑅𝑎)
=
𝑅𝑎 + 𝑅𝑏 + 𝑅𝑐
(3)
Adding Eqs. (2b) and (3) gives
𝑅𝑏𝑅𝑐
𝑅1 = 𝑅
+ 𝑅 + 𝑅
𝑎 𝑏 𝑐
(4)
And subtracting Eq. (3) from Eq. (2b) yields
𝑅𝑐𝑅𝑎
𝑅2 = 𝑅
+ 𝑅 + 𝑅
𝑎 𝑏 𝑐
(5)
Subtracting Eq. (4) from Eq. (2a), we obtain
𝑅𝑎𝑅𝑏
𝑅3 = 𝑅
+ 𝑅 + 𝑅
𝑎 𝑏 𝑐
(6)
We do not need to memorize Eqs. (4) to (6). To transform a network to Y, we create an extra node n as shown in Fig. 2.49 and follow this conversion rule:
Each resistor in the Y network is the product of the resistors in the two adjacent ∆ branches, divided by the sum of the three ∆ resistors.
One can follow this rule and obtain Eqs. (4) to (6) from Fig. 4.
Fig. 4
Superposition of Y and networks as an aid in transforming one to the other.

## Slide 5
5
Wye to Delta Conversion
To obtain the relationships necessary to convert from a Y to a ∆, first divide Eq. (6) by Eq. (4):
𝑅3 (𝑅𝑎𝑅𝑏)⁄(𝑅𝑎 + 𝑅𝑏 + 𝑅𝑐) 𝑅𝑎
𝑅 = (𝑅 𝑅 )⁄(𝑅 + 𝑅 + 𝑅 ) = 𝑅
1 𝑏 𝑐 𝑎 𝑏 𝑐 𝐶
Or
𝑎
𝑅𝑐𝑅3
𝑅 =
𝑅1
Then divide Eq. (6) by Eq. (5)
𝑅3 (𝑅𝑎𝑅𝑏)⁄(𝑅𝑎 + 𝑅𝑏 + 𝑅𝑐) 𝑅𝑏
𝑅 = (𝑅 𝑅 )⁄(𝑅 + 𝑅 + 𝑅 ) = 𝑅
2 𝑎 𝑐 𝑎 𝑏 𝑐 𝑐
Or
𝑏
𝑅𝑐𝑅3
𝑅 =
𝑅2
Substituting for 𝑅𝑎 and 𝑅𝑏 in Eq. (5) yields
2
𝑅 =
(𝑅𝑐𝑅3⁄𝑅1)𝑅𝑐
(𝑅3𝑅𝑐⁄𝑅2) + (𝑅𝑐𝑅3⁄𝑅1) + 𝑅𝑐 (𝑅3⁄𝑅1)𝑅𝑐
= (𝑅 ⁄𝑅 ) + (𝑅 ⁄𝑅 ) + 1
3 2 3 1
Placing these over a common denominator, we obtain
2
𝑅 =
(𝑅3𝑅𝑐⁄𝑅1)
1 2
(𝑅 𝑅 + 𝑅 𝑅 + 𝑅 𝑅 )⁄(𝑅 𝑅 )
=
1 3 2 3 1 2
𝑅2𝑅3𝑅𝑐
𝑅1𝑅2 + 𝑅1𝑅3 + 𝑅2𝑅3
And
𝑅𝑐 =
𝑅1𝑅2 + 𝑅1𝑅3 + 𝑅2𝑅3
𝑅
3
(7)
We follow the same procedure for 𝑅𝑏 and 𝑅𝑎:

## Slide 6
6
𝑅𝑎 =
𝑅1𝑅2 + 𝑅1𝑅3 + 𝑅2𝑅3
𝑅
1
(8)
And
𝑅𝑏 =
𝑅1𝑅2 + 𝑅1𝑅3 + 𝑅2𝑅3
𝑅
2
(9)
Each resistor in the ∆ network is the sum of all possible products of Y resistors taken two at a time, divided by the opposite Y resistor.
The Y and ∆ networks are said to be balanced when
𝑅1 = 𝑅2 = 𝑅3 = 𝑅𝑌, 𝑅𝑎 = 𝑅𝑏 = 𝑅𝑐 = 𝑅∆,
Under these conditions, conversion formulas become
𝑅∆
𝑅𝑌 = 3 𝑜𝑟 𝑅∆ = 3𝑅𝑌
Example 1: Convert the ∆ network in Fig. 5a to an equivalent Y network
Fig.5
For Example 5: (a) original ∆ network, (b) Y equivalent network.

## Slide 7
7
Solution:
1
𝑅 =
=
𝑅𝑏𝑅𝑐 10 × 25
𝑅𝑎 + 𝑅𝑏 + 𝑅𝑐 15 + 10 + 25 50
250
= = 5
2
𝑅 =
=
𝑅𝑐𝑅𝑎 25 × 15
𝑅𝑎 + 𝑅𝑏 + 𝑅𝑐 15 + 10 + 25 50
375
= = 7.5
3
𝑅 =
=
𝑅𝑎𝑅𝑏 10 × 15
𝑅𝑎 + 𝑅𝑏 + 𝑅𝑐 15 + 10 + 25 50
150
= = 3
The equivalent Y network is shown in Fig. 5(b).
Example 2: Obtain the equivalent resistance 𝑹𝒂𝒃 for the circuit in Fig. 6 and use it to find current i.
Fig. 6
H.W. 1:For the bridge network in Fig. 7, find 𝑹𝒂𝒃 and i.
𝐴𝑛𝑠𝑤𝑒𝑟: 40, 2.5 𝐴.