## Slide 1
Department of Computer Engineering
College of Engineering
University of Diyala
GNSS Application
3rd Lecture
GPS - NMEA Sentence
By:
Dr. Ali Albu-Rghaif

## Slide 2: Outline
Introduction to NMEA Sentences
Purpose of NMEA Sentences
Type of NMEA Sentences
Structure of NMEA Sentences
    GGA Sentence

## Slide 3: Introduction to NMEA Sentences
The National Marine Electronics Association (NMEA) developed a standard that defines the interface between various pieces of marine electronic equipment and navigational computers, allowing them to talk together and share vital information.
Talker  GPS Receiver
Listener Computer, Plotter, Radar, Smartphone.
NMEA standard is 4800 b/s (bit per second rate) with 8 bits of data.
Introduction to GPS The Global Positioning System

## Slide 4: Purpose of NMEA Sentences
NMEA is to give equipment users the ability to mix and match hardware and software.
NMEA-formatted GPS data also makes life easier for software developers to write software for a wide variety of GPS receivers instead of having to write a custom interface for each GPS receiver.
Without NMEA, it would be time-consuming and expensive to write and maintain such software.
Introduction to GPS The Global Positioning System

## Slide 5: Type of NMEA Sentences
Some of the standard NMEA "sentences" include:
Sentences | Meaning
AAM | Waypoint arrival alarm
APA | Autopilot format A
APB | Autopilot format B
BOD | Bearing, origin to destination
BWC | Bearing and distance to waypoint, great circle
BWR | Bearing and distance to waypoint, rhumb line (overridden by BWC if available)
DBT | Depth below transducer
DPT | Depth of water
GGA | Global Positioning System Fix Data
Introduction to GPS The Global Positioning System

## Slide 6: Type of NMEA Sentences
Sentences | Meaning
GLL | Geographic position, latitude and longitude (and time)
GSA | GPS DOP and active satellites
GSV | Satellites in view
HDM | Heading, magnetic north
HDT | Heading, true north
HSC | Steer to heading
MTW | Mean water temperature
RMB | Recommended minimum navigation info when dest. waypoint is active
RMC | Recommended minimum specific GPS/Transit data
VTG | Track made good and ground speed
WCV | Waypoint closure velocity
WPL | Waypoint location
Introduction to GPS The Global Positioning System

## Slide 7: Structure of NMEA Sentences
To understand the NMEA message structure, let’s examine the popular $GPGGA message.
This particular message was output from an RTK GPS receiver:
$GPGGA,181908.00,3404.7041778,N,07044.3966270,W,4,13,1.00,495.144,M,29.200,M,0.10,0000*40
$ : All NMEA messages start with the $ character
GP: represent that it is a GPS position (GL would denote GLONASS).
181908.00: is the time stamp: UTC time in hhmmss.ss.
3404.7041778: is the latitude in the DDMM.MMMMM format.
N: denotes north latitude.
Introduction to GPS The Global Positioning System

## Slide 8: Structure of NMEA Sentences
$GPGGA,181908.00,3404.7041778,N,07044.3966270,W,4,13,1.00,495.144,M,29.200,M,0.10,0000*40
07044.3966270: is the longitude in the DDDMM.MMMMM format.
W: denotes west longitude.
4: denotes the Quality Indicator:
1 = Uncorrected coordinate
2 = Differentially correct coordinate (e.g., WAAS, DGPS)
4 = RTK Fix coordinate (centimeter precision)
5 = RTK Float (decimeter precision.
13: denotes number of satellites used in the coordinate.
Introduction to GPS The Global Positioning System

## Slide 9: Structure of NMEA Sentences
$GPGGA,181908.00,3404.7041778,N,07044.3966270,W,4,13,1.00,495.144,M,29.200,M,0.10,0000*40
1.0: denotes the HDOP (horizontal dilution of precision)
495.144: denotes altitude of the antenna.
M: denotes units of altitude (eg. Meters or Feet)
29.200: denotes the geoidal separation (subtract this from the altitude of the antenna to arrive at the Height Above Ellipsoid (HAE).
M: denotes the units used by the geoidal separation.
1.0: denotes the age of the correction (if any).
0000: denotes the correction station ID (if any).
*40: denotes the checksum.
Introduction to GPS The Global Positioning System

## Slide 10: Summary
You have learned what is the NMEA Sentences and what are the purpose
Also the Types of NMEA sentences have been illustrated
Eventually, you be able to read/understand the NMEA sentences by knowing the structure of the GGA sentence

## Slide 11
Reference
Introduction to GPS The Global Positioning System
Artech House
Boston  London