## Slide 1: محاضرة بمادة التقنيات الرقمية
م. د حسين فالح مهدي
جامعة ديالى
كلية الهندسة –قسم هندسة الحاسوب
2022-2023
NUMBER SYSTEM -2-

## Slide 2: Operation on systems
Addition
1) Binary number system
1001+0001 =1010
2) Octal number system
Example : 357 ( 7+6= 13-8=5 and add carry1)
+ 276 (1+5+7=13-8=5 and add carry1)
655 (1+3+2=6 OK)

## Slide 3: Operation on systems
3) Hexadecimal number system
AB2F (F+C = 15+12=27-16=11=B with Carry1)
+12EC ( 1+2+E=1+2+14=17-16=1 with Carry1)
BE1B ( 1+B+2= 1+11+2=14=E )
(A+1=10+1=11=B)

## Slide 4: Operation on systems
Subtraction
1) Binary number system
1011 1011 0110 0110
-0110---1’s - +1001 -1011 --1’s - +0100
1 0100 0 1010
+ 1 1’s -0101
0101

## Slide 5: Operation on systems
Example/ solve using 2’s complement:
1011 1011
-0110---1’s +1=2’s - + 1010
1 0101
0110 0110
-1011 -- 1’s +1=2’s -- + 0101
0 1011 -- 1’s +1=2’s --– (-0101)
Discard

## Slide 6: Operation on systems
2) Octal number system
Ex/ Subtract the following numbers
750 711 4321
- 76 - 377 - 2567
652 312 1532
H.W/ Ex/ Subtract the last Example using 7’s and 8’s complement

## Slide 7: Operation on systems
Example/ solve the following usinge using 7’s and 8’s complement
750 750 750 750
- 76 ------7’s --- +701 -76 ----8’s--- +702
1 651 1 652
(7+7=14-8=6) 1 Discard
652

## Slide 8: Operation on systems
Example/ solve the following usinge using 7’s and 8’s complement
76 76 76 76
- 750 ------7’s -- +027 -750 ----8’s--- +030
0125 (7+3=10-8=2) 0 126
(7+6=13-8=5) 7’s (-652) 8’s (-652)
(1+7+2=10-8=2)

## Slide 9: Operation on systems
3)Hexadecimal number system
Example /Subtract the following hexadecimal numbers using 15’s and 16’s complements:
32FB 32FB (15+1=16-16=0 WITH CARRY1)
- FEF ---15’s F010 (3+15=18-16=2 WITH CARRY1)
230C 1230B
1
230C

## Slide 10: Operation on systems
32FB 32FB (15+1=16-16=0 WITH CARRY1)
- FEF ---16’s F011 (3+15=18-16=2 WITH CARRY1)
230C 1 230C
Discard
Example /Subtract the following hexadecimal numbers using 15’s and 16’s complements:
FEF 0FEF (15+4=19-16=3 WITH CARRY1)
- 32FB ---15’s CD04 (13+15=28-16=12 WITH CARRY1)
230C 0 DCF3
15’S (-230C )

## Slide 11: Operation on systems
FEF 0FEF (15+5=20-16=4 WITH CARRY1)
- 32FB ---16’s CD05 (13+15=28-16=12 WITH CARRY1)
230C 0 DCF4
16’S (- 230C )

## Slide 12: Binary Coded Decimal
Decimal digits | Bcd codes 8421 | 2421 | 84-2-1 | 7421 | 6311 | 4221 | 5421
0 | 0000 | 0000 | 0000 | 0000 | 0000 | 0000 | 0000
1 | 0001 | 0001 | 0111 | 0001 | 0001 | 0001 | 0001
2 | 0010 | 0010 | 0110 | 0010 | 0011 | 0010 | 0010
3 | 0011 | 0011 | 0101 | 0011 | 0100 | 0011 | 0011
4 | 0100 | 0100 | 0100 | 0100 | 0110 | 1000 | 0100
5 | 0101 | 1011 | 1011 | 0101 | 0111 | 0111 | 1000
6 | 0110 | 1100 | 1010 | 0110 | 1000 | 1100 | 1001
7 | 0111 | 1101 | 1001 | 1000 | 1001 | 1101 | 1010
8 | 1000 | 1110 | 1000 | 1001 | 1011 | 1110 | 1011
9 | 1001 | 1111 | 1111 | 1010 | 1100 | 1111 | 1100

## Slide 13: BCD-to-Binary Conversion
• BCD number: 0010 1001.0111 0101.
• Corresponding decimal number: 29.75.
• Therefore, (0010 1001.0111 0101)BCD =(11101.11)2.
H.w / convert (11100.01)2 to BCD?

## Slide 14: Operation of BCD codecs
Addition
Ex40/ Add the following (45)10 + (67)10 as BCD
Sol :
45 0100 0101,
67 0110 0111
When the result of the BCD is larger than 1001 then add 0110 to that result and find the final result
0100 0101
+ 0110 0111
1010 1100
+ 0110 0110
1 0001 0010 (112) BCD

## Slide 15: Operation of BCD codecs
Subtraction
Ex/ Find
1)(678)10 + (569)10,
2) (678)10 - (569)10 as BCD
Sol: 1-)
(678)10 = 0110 0111 1000,
(569)10 = 0101 01101001
When carry occurs from digit to another then add 0110 to that result and find the result.
0110 0111 1000
+ 0101 0110 1001
1011 1110 0001
+ 0110 0110 0110
1 0010 0100 0111 (1247)10

## Slide 16: Operation of BCD codecs
2-) (678)10 - (569)10
When the one number take one from its neighbor then subtract 0110 from it to obtain the final result.
0110 0111 1000
- 0101 0110 1001
0001 0000 1111
- 0110
- 0001 0000 1001 (-109)

## Slide 17: Excess-3 codes
Decimal digits | Excess-3 codes
0 | 0011
1 | 0100
2 | 0101
3 | 0110
4 | 0111
5 | 1000
6 | 1001
7 | 1010
8 | 1011
9 | 1100

## Slide 18: Operation of Ex-3 codes
Addition
Ex / Solve the following (87)10 + (45)10 as Ex-3 code
Sol: (87) to BCD (1000 0111) to Ex- 3 (1011 1010)
(45) to BCD (0100 0101) to Ex- 3 (0111 1000)
Each number does not produce carry then (0011) must be subtracted from it to obtain the result.
1011 1010
+ 0111 1000
1 0011 0010
+ 0011 0011
1 0110 0101

## Slide 19: Operation of Ex-3 codes
Ex / Solve the following (43)10 + (12)10 as Ex-3 code
(43) to BCD (0100 0011) to Ex- 3 (0111 0110)
(12) to BCD (0001 0010) to Ex- 3 (0100 0101)
Each number does not produce carry then (0011) must be subtracted from it to obtain the result.
0111 0110
+ 0100 0101
1011 1011
- 0011 0011
1000 1000 (88)10

## Slide 20: Operation of Ex-3 codes
Subtraction
EX/ Find (68)10 – (34)10
(68) to BCD (0110 1000) to Ex- 3 (1001 1011)
(39) to BCD (0011 1001) to Ex- 3 (0110 1100)
Each number take one from neighbor then (0011) must be subtracted from it and (0011) is added to the number that does not take one from neighbor .
1001 1011
- 0110 1100
0010 1111
+0011- 0011
0101 1100

## Slide 21: Gray codes
Decimal Binary Gray Decimal Binary Gray
0 0000 0000 8 1000 1100
1 0001 0001 9 1001 1101
2 0010 0011 10 1010 1111
3 0011 0010 11 1011 1110
4 0100 0110 12 1100 1010
5 0101 0111 13 1101 1011
6 0110 0101 14 1110 1001
7 0111 0100 15 1111 1000

## Slide 22: Conversion from Binary to Gray and Gray to Binary

## Slide 23
Thank you